## Slide 1: Ensemble and Hybrid Modeling
RAVEN Workshop

## Slide 2: Outline
RAVEN models: brief overview
Ensemble Modeling
  Overview
  Characteristics and limitations
  Hands-on
Hybrid Modeling
  Overview
  Characteristics
  Hands-on

## Slide 3: RAVEN models: overview

## Slide 4: RAVEN models: a quick introduction
RAVEN categorizes in its Models entity the following sub-entities:
  Codes:
    Aimed to interface with physical codes (e.g. RELAP5-3D, etc.)
  ROMs:
    Aimed to emulate the response of a system based on a simplified mathematical representation
  External Models:
    Aimed to provide to the user an easy way to implement sets of equations directly in RAVEN
  Post-Processors:
    Aimed to analyze the generated datasets (e.g. Statistical moments, Data Mining, etc.)
  Ensemble Models:
    Aimed to assemble multiple models
  Hybrid Models:
    Automatic model selections

## Slide 5: RAVEN ensemble modeling

## Slide 6: Ensemble Modeling Motivations
In several cases multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others
In order to face this “problem” in the RAVEN framework, a new model category (e.g. class), named EnsembleModel, has been designed
This class is able to assemble multiple models of other categories (i.e. Code, External Model, ROM), identifying:
  the input/output connections
  the order of execution
  the parallel execution strategy for each sub-model
EnsembleModel
Physics 1
Physics 2

## Slide 7: Ensemble Model
A new model entity (e.g., class), named EnsembleModel, has been developed:
  Assemble multiple models of other categories, identifying the input/output connections and the order of execution
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 8: Ensemble Model: Main Characteristics
The EnsembleModel entity has the following main characteristics:
  Ability to link all the RAVEN Models:
    Codes, ROMs, ExternalModels
  Practical no limit on the number of Models in the Ensemble configuration
  Capability to link the different Models through both scalar and vector variables (e.g. Max Cladding Temperature (scalar) or Power history (vector))
  Capability to transfer meta-data from the different models (e.g. restart files, etc.)
The current EnsembleModel entity is not indicated to handle high-density field data

## Slide 9
Model 1
Model N-1
Model N
Model 1
Model 2
Model 3
  Ensemble Model: Chain of Models
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 10
  Ensemble Model: Non Linear
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 11: Ensemble model for Multi-Unit Power Plant: 1st Configuration
Dynamic PRA for a Station Black Out Multi-Unit scenario
Plant Logic Model
Unit 1
Unit 2
Unit 3
PWR1
SFP1
PWR2
SFP2
PWR3
SFP3
RAVEN ensemble model

## Slide 12: Employing Ensemble modeling in RAVEN

## Slide 13: Getting on the same page
This workshop will include interactive examples
paths given starting at raven
Slides are provided as well:
~> cd projects/raven
~/projects/raven> git checkout workshop_2018
~/projects/raven> git pull
raven/doc/workshop/ensembleModels

## Slide 14: Example: External Model A
RAVEN samples codes
For experiment, we’ve provided some physics in a code
projectile.py
Given:
  y0, the initial vertical position
  x0, the initial horizontal position
  , the launch angle
  v0, the launch velocity
Calculates:
  , the horizontal position throughout the arc
  , the vertical position throughout the arc
  , the range or furthest point reached
  , the time of flight

## Slide 15: Example: External Model B
Model: kineticEnergy.py
  Input: energy (E), and mass (m)
  Output: v0
Model B
Model A
v0

## Slide 16: Workflow
Create EnsembleModel
Sample the model
Plot results

## Slide 17: Create an Ensemble model
Samplers
Models
Distributions
Steps
Databases
DataObjects
<Distributions>
<Normal name=’angle_d'>
<mean>45</mean>
<sigma>5</sigma>
<upperBound>5</upperBound>
<lowerBound>85</lowerBound>
</Normal>
</Distributions>
Distribution specifications
OutStreams
Add distributions for mass and energy

## Slide 18: Create an Ensemble model
Models
Distributions
<Models>
...
<ExternalModel name=’projectile' subType=’’ ModuleToLoad=’../../projectile’>
<variables>x0,v0,y0,angle,x,y,r,t</variables>
</ExternalModel>
<ExternalModel name=’kineticEnergy’ subType=’’ ModuleToLoad=’../../kineticEnergy’>
<variables>energy,mass,v0</variables>
</ExternalModel>
...
</Models>
Samplers
Steps
Databases
DataObjects
OutStreams
List of Models we are going to use

## Slide 19: Create an Ensemble model
Models
Distributions
<Models>
...
<EnsembleModel name=’ensembleModel' subType=’’>
<Model class=’Models' type=’ExternalModel’>
projectile
<Input class=“DataObjects” type=“PointSet”>inputHolder</Input >
<TargetEvaluation class=’DataObjects’
type=’PointSet’>projectileContainer
</TargetEvaluation>
</Model>
<Model class=’Models' type=’ExternalModel’>
kineticEnergy
<Input class=“DataObjects” type=“PointSet”>inputHolder</Input >
<TargetEvaluation class=’DataObjects’ type=’PointSet’>
KEnergyContainer</TargetEvaluation>
</Model>
</EnsembleModel>
...
</Models>
Samplers
Steps
Databases
DataObjects
OutStreams
Inputs of this model
Exclusive output

## Slide 20: Create an Ensemble model
DataObjects
Distributions
Samplers
Steps
Databases
Models
OutStreams
<DataObjects>
<PointSet name=’projectileContainer'>
<Input>x0,y0,v0,angle</Input>
<Output>r,t</Output>
</PointSet>
<PointSet
name=’KEnergyContainer'>
<Input>mass,energy</Input>
<Output>v0</Output>
</PointSet>
</DataObjects>
Link

## Slide 21: Create an Ensemble model
Create EnsembleModel
Add DataObjects for TargetEvaluation
Plot using OutStreams
  r ~ f(v0, angle, t)

## Slide 22
Let’s run the code…

## Slide 23: Hybrid Model

## Slide 24: Hybrid-Model (automatic selection ROM/physical model)
The HybridModel is designed to combine multiple surrogate models and any other Model (i.e. high-fidelity model) leveraging the EnsembleModel infrastructure, deciding which of the Model needs to be evaluated based on the model validation score.

## Slide 25: Cross-Validation for assessing Surrogate Models validity
Take out some of the training set
  Train on the remaining training set
  Test on the excluded instances
  Cross-validation
Train
Test
Dataset
Cross Validation
Compute a score (e.g. R2)

## Slide 26: Model validation RAVEN scheme
Mean Absolute Error score (Cross-validation) as function of # samples

## Slide 27: Projectile Model
RAVEN samples codes
For experiment, we’ve provided some physics in a code
projectile.py
Given:
  y0, the initial vertical position
  x0, the initial horizontal position
  , the launch angle
  v0, the launch velocity
Calculates:
  , the horizontal position throughout the arc
  , the vertical position throughout the arc
  , the range or furthest point reached
  , the time of flight

## Slide 28: ROM: Inverse Distance Weight
See section 17.3.6 NDinvDistWeight
Interpolating function

## Slide 29: Workflow
Create HybridModel
Sample the model
Plot results

## Slide 30: Create a Hybrid model
Models
Distributions
<Models>
...
<ExternalModel name=’projectile' subType=’’ ModuleToLoad=’../../projectile’>
<variables>angle,x,y,r,t</variables>
</ExternalModel>
<ROM name=’IDW’ subType=’’>
<Features>angle</Features>
<Target>r</Target>
<p>3</p>
</ROM>
...
</Models>
Samplers
Steps
Databases
DataObjects
OutStreams
List of Models we are going to use

## Slide 31: Create a Hybrid model
Models
Distributions
Samplers
Steps
Databases
DataObjects
OutStreams

## Slide 32: Create a Hybrid model
Models
Distributions
Samplers
Steps
Databases
DataObjects
OutStreams

## Slide 33: Create a Hybrid model
Models
Distributions
Samplers
Steps
Databases
DataObjects
OutStreams
Metrics

## Slide 34: Create a Hybrid model
DataObjects
Distributions
Samplers
Steps
Databases
Models
OutStreams
<DataObjects>
<PointSet name=’outMC'>
<Input>angle</Input>
<Output>r</Output>
</PointSet>
<PointSet
name=’projectileContainer'>
<Input>angle</Input>
<Output>r</Output>
</PointSet>
</DataObjects>
Link

## Slide 35: Create A Hybrid Model
/raven/doc/workshop/ensembleModels/inputs/exercises/2_hybrid_model.xml
Create a hybrid model: section 17.7
Create a cross validation PostProcessor: section 17.5.14
Create a metric: section 19
Update DataObjects and Steps

## Slide 36
Let’s run the code…

## Slide 37: Thank you Questions?