## Slide 1: Reduced Order and Ensemble Modeling
RAVEN Workshop
PHYSOR 2016 – May 1st 2016, Sun Valley (ID)

## Slide 2: Outline
RAVEN models: brief overview
Reduced Order Modeling
  Brief introduction
  When we can apply them
  ROMs and RAVEN
Ensemble Modeling
Application examples of Reduced Order and Ensemble Modeling

## Slide 3: RAVEN models: overview

## Slide 4: RAVEN models: a quick introduction
RAVEN categorizes in its Models entity the following sub-entities:
  Codes:
    Aimed to interface with physical codes (e.g. RELAP5-3D, etc.)
  ROMs:
    Aimed to emulate the response of a system based on a simplified mathematical representation
  External Models:
    Aimed to provide to the user an easy way to implement sets of equations directly in RAVEN
  Post-Processors:
    Aimed to analyze the generated datasets (e.g. Statistical moments, Data Mining, etc.)
  Ensemble Models:
    Aimed to assemble multiple models

## Slide 5
Reduced Order Modeling

## Slide 6: ROMs: a Quick Introduction
Consider a set of N data points
Build a surrogate model
  Reduced Order Model
Inputs: Initial and boundary conditions
Output: Simulation outcome (success/failure, max clad temperature)
≅
DataObjects
(PointSet)

## Slide 7: ROMs: a Quick Introduction
Basically we are trying to reduce the complexity of the original model
Pros:
  Much faster computation of the output variable
Cons:
  Presence of error in the ROM computed values
≅
Original data (e.g., RELAP5)
ROM (e.g., quadratic regressor)

## Slide 8: Classes of ROMs
Model-Based
  Prediction is performed using a blend of interpolation and regression algorithms
  Examples:
    Gaussian Process Models (GPMs)
    Spline interpolator
Data-Based
  Prediction is performed by solely considering the input data by using data searching algorithms
  Examples:
    Nearest neighbor

## Slide 9: ROMs: Applications
Basic steps:
  Sample original model
  Train the ROM
  Perform desired analysis with the ROM
  instead of the original model
Range of applications:
  Uncertainty quantification / Sensitivity analysis
  Probabilistic Risk Analysis (PRA)
  Accelerator for stochastic analysis (adaptive sampling)
  Prediction models
Input x
Output y

## Slide 10: ROMs Available in RAVEN
  External libraries: Scikit-learn (http://scikit-learn.org)
  Open source machine learning library for Python
  Library for data mining and data analysis
  Built on NumPy and SciPy
Internally C++ developed libraries: CROW
  Generalized Polynomial Chaos (subject of a later presentation)
  Multi-dimensional interpolators
    ND Spline
    ND Inverse-Weight

## Slide 11: Scikit-Learn Library
Available:
  Classification: identifying to which category an object belongs
  Regression: predicting a continuous-valued attribute
  Data clustering: grouping similar objects into sets
  Dimensionality reduction: reducing the number of random variables
  Data pre-processing: feature extraction and normalization
Examples:
  Linear regression models
  Support Vector Machines
  Multi-Class classifiers
  Naïve Bayes
  Neighbors classifiers
  Tree classifiers
Notes: Add backup slides for some algorithms GPM and SVM

## Slide 12: Scikit-Learn Library
Classification
  Starting point: set of data points with labels
  [features, class]i
  Objective: identify which class a new point [features] belong
Clustering
  Starting point: set of data points
  [features]I
  Objective: group data points based on a specific distance metrics
Y
(μ1,σ12)
(μ2,σ22)
X
Notes: Add backup slides for some algorithms GPM and SVM

## Slide 13: Scikit-Learn Library
  Starting point: set of data points
  [features]i
Cardinality reduction
  Objective: identify the most relevant features that keep data points unique
  Outcome: Location of the points on the reduced space (e.g., line)
Regression
  Objective: estimate the relationships among variables via a statistical process
  Outcome: coefficients of the reduced space (e.g., m and c for linear interpolator )
Source: scikit-learn.org
Notes: Add backup slides for some algorithms GPM and SVM

## Slide 14: Multi-Dimensional Interpolators
CROW: Internally developed C++ library
Interpolation on any dimension
Response surface is created as an interpolation function given a set of data points defined on:
  Sparse grid
  Cartesian grid
Extension of the known 1-D interpolation schemes

## Slide 15: Multi-Dimensional Interpolators
Two classes of algorithms
  Inverse-Weight
    No interpolation kernel is defined
    Defined on sparse grid
  Multi-Dimensional Spline
    Defined on cartesian grid
    Based on multi-dimensional spline kernel
    Continuity of the derivative is preserved
where:

## Slide 16: RAVEN reduced order modeling: examples

## Slide 17: Test cases
Surrogate Models chosen:
  Support Vector Machines (SVM)
  K Nearest Neighbors (KNN)
Test cases:
  PWR system; LOOP + SBO scenario
    DG failure time
    PG recovery time
  2 analytical cases
  1 discontinuous test case

## Slide 18: PWR SBO Test case: SVM
Iteration
1
30
60
185
Initial training samples
Initial estimate of the limit surface

## Slide 19: Discontinuous Test case: KNN
Iteration
1
150
450
675
Initial estimate of the limit surface
Initial training samples

## Slide 20: Comparison Criteria
Initial conditions
  Fixed value for probability convergence criteria: 1.0 E-4
  Identical initial training points
Observe for each ROM (KNN and SVM)
  Number of samples required
  Error of probability value within limit surface boundaries

## Slide 21: Results
PWR SBO
Multiple Regions
Discontinuous
 | # iterations | error
SVM | 270 | 3.45 E-4
KNN | 328 | 3.10 E-3
 | # iterations | error
SVM | 199 | 3.54 E-2
KNN | 556 | 4.50 E-3
 | # iterations | error
SVM | 645 | 4.11 E-3
KNN | 675 | 8.69 E-2

## Slide 22: RAVEN ensemble modeling

## Slide 23: Ensemble Model
A new model entity (e.g., class), named EnsembleModel, has been developed:
  Assemble multiple models of other categories, identifying the input/output connections and the order of execution
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 24
Model 1
Model N-1
Model N
Model 1
Model 2
Model 3
  Ensemble Model: Chain of Models
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 25
  Ensemble Model: Non Linear
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 26: RAVEN ensemble modeling: 3 simple examples

## Slide 27
1-Dimensional heat conduction transient (in a slab of thickness L=1 m):
  EM1, heat conduction partial differential equation:
  EM2, thermal conductivity (input of EM1) as function of the average temperature in the slab boundary conditions:
EM1
EM2
  Ensemble Model: Example 1

## Slide 28
1-Dimensional heat conduction transient (in a slab of thickness L=1 m):
  EM1, heat conduction partial differential equation:
  EM2, thermal conductivity (input of EM1) as function of the average temperature in the slab (solution):
EM1
EM2
  Ensemble Model: Example 2

## Slide 29
Also codes can be used in the Ensemble modeling.
  EM1: Code, Analytical Bateman
    Transmutation
  EM2: External Model, compute the sum of the final outcomes of EM1
EM1
EM2
  Ensemble Model: Example 3

## Slide 30: Employing Reduced Order and Ensemble modeling in RAVEN

## Slide 31: ROMs

## Slide 32: ROM Modeling Within RAVEN
All modeling steps that involve ROMs are available in RAVEN
  Create ROMs from a database
  Compare the responses

## Slide 33: Exercise: Create a ROM of an “High-fidelity” model and use it

## Slide 34: Workflow
Sample model
Input File name: ROM_example.xml
Create database
Train a ROM
Sample a ROM
Compare Results

## Slide 35: Create a ROM of an “High-fidelity” model and use it
Samplers
Models
Distributions
Steps
Databases
DataObjects
<Distributions>
<Uniform name=’uni'>
<upperBound>1.0</upperBound>
<lowerBound>0.0</lowerBound>
</Uniform>
</Distributions>
Distribution specifications
OutStreams

## Slide 36: Create a ROM of an “High-fidelity” model and use it
Models
Distributions
<Models>
<ExternalModel name=’attenuation' subType=’’ ModuleToLoad=’poly’>
<variables>
y1,
y2,
ans
</variables>
</ExternalModel>
<ROM name=’a_ROM' subType=’NDinvDistWeight’>
<Features>
y1,y2
</Features>
<Targets>
ans
</Targets>
<p>
3
</p>
</ROM>
</Models>
Samplers
Steps
Databases
DataObjects
Input variables
Output variables
File name:
poly.py
Input Space
Output Space
ROM parameters
OutStreams

## Slide 37: Create a ROM of an “High-fidelity” model and use it
Samplers
Distributions
<Samplers>
<Grid name='Grid_sampler'>
<variable name=’y1' >
<distribution>uni</distribution>
<grid type='value’ construction='equal' steps='5'>0.0 1.0</grid>
</variable>
<variable name=’y2' >
<distribution>uni</distribution>
<grid type=’CDF’ construction='equal' steps='5'>0.0 1.0</grid>
</variable>
</Grid>
</Samplers>
Models
Steps
Databases
DataObjects
<variable name>
<distribution>
<grid points>
OutStreams

## Slide 38: Create a ROM of an “High-fidelity” model and use it
Distributions
<DataObjects>
<PointSet name=’outGRID'>
<Input>y1,y2</Input>
<Output>ans</Output>
</PointSet>
<PointSet name=’outGRID_from_db'>
<Input>y1,y2</Input>
<Output>ans</Output>
</PointSet>
<PointSet name=’outGRID_ROM'>
<Input>y1,y2</Input>
<Output>ans</Output>
</PointSet>
<PointSet name='inputPlaceHolder'>
<Input>y1,y2</Input>
<Output>OutputPlaceHolder</Output>
</PointSet >
</DataObjects>
Databases
DataObjects
Samplers
Models
Steps
<DataObjects>
<Input>
<Output>
<Databases>
<HDF5
name='out_db’
readMode=’overwrite’
/>
</Databases>
Overwrite or update?
OutStreams

## Slide 39: Create a ROM of an “High-fidelity” model and use it
Distributions
<OutStreams>
<Print name=’out_dump'>
<type>csv</type>
<source>outGrid</source>
</Print>
<Plot name=’plotResponse’ dim=’3’ >
<plotSettings>
<plot>
<type>scatter</type>
<x>outGRID|Input|y1</x>
<y>outGRID|Input|y2</y>
<z>outGRID|Output|ans</z>
</plot>
</plotSettings>
<actions>
<how>screen,png</how>
</actions>
</Plot>
</OutStreams>
Samplers
Models
Steps
CSV or XML
Databases
OutStreams
DataObjects
Which DataObject we want to print?
2D or 3D
Output format
Plot Type
x y z variables

## Slide 40: Create a ROM of an “High-fidelity” model and use it
Distributions
Steps
Samplers
Models
Databases
DataObjects
<Steps>
<MultiRun name=’sampleModel'>
<Input class='DataObjects' type=’Point' >inputPlaceHolder</Input>
<Model class='Models' type='ExternalModel’>attenuation</Model>
<Sampler class='Samplers' type='Grid' >Grid_sampler</Sampler>
<Output class='DataObjects’ type=’PointSet’ >outGRID</Output>
<Output class='Databases' type='HDF5' >out_db</Output>
<Output class='OutStreams' type='Print' >out_dump</Output>
<Output class='OutStreams' type='Plot' >plotResponse</Output>
</MultiRun>
<IOStep name=’extractDatabase'>
<Input class='Databases' type='HDF5' >out_db</Input>
<Output class='DataObjects’ type=’PointSet’ >outGRID_from_db</Output>
</IOStep>
…
(cont. in next slide)
…
</Steps>
OutStreams

## Slide 41: Create a ROM of an “High-fidelity” model and use it
Distributions
Steps
Samplers
Models
Databases
DataObjects
<Steps>
…
(cont. from previous slide)
…
<RomTrainer name=’trainROM'>
<Input class='DataObjects’ type=’PointSet’ >outGRID_from_db</Input>
<Output class='Models' type=’ROM’ >a_ROM</Output>
</RomTrainer>
<MultiRun name=’sampleROM'>
<Input class='DataObjects' type=’Point' >inputPlaceHolder</Input>
<Model class='Models' type='ROM’ >a_ROM</Model>
<Sampler class='Samplers' type='Grid' >Grid_sampler</Sampler>
<Output class='DataObjects’ type=’PointSet’ >outGRID_ROM</Output>
<Output class='OutStreams' type='Plot' >plot_ROM_LS</Output>
</MultiRun>
</Steps>
OutStreams

## Slide 42: Create a ROM of an “High-fidelity” model and use it
Let’s run the code…

## Slide 43: Thank you Questions?