## Slide 1: Reduced Order and Ensemble Modeling
RAVEN Workshop
PHYSOR 2016 – May 1st 2016, Sun Valley (ID)

## Slide 2: Outline
RAVEN models: brief overview
Reduced Order Modeling
  Brief introduction
  When we can apply them
  ROMs and RAVEN
Ensemble Modeling
Application examples of Reduced Order and Ensemble Modeling

## Slide 3: RAVEN models: overview

## Slide 4: RAVEN models: a quick introduction
RAVEN categorizes in its Models entity the following sub-entities:
  Codes:
    Aimed to interface with physical codes (e.g. RELAP5-3D, etc.)
  ROMs:
    Aimed to emulate the response of a system based on a simplified mathematical representation
  External Models:
    Aimed to provide to the user an easy way to implement sets of equations directly in RAVEN
  Post-Processors:
    Aimed to analyze the generated datasets (e.g. Statistical moments, Data Mining, etc.)
  Ensemble Models:
    Aimed to assemble multiple models

## Slide 5
Reduced Order Modeling

## Slide 6: ROMs: a Quick Introduction
Consider a set of N data points
Build a surrogate model
  Reduced Order Model
Inputs: Initial and boundary conditions
Output: Simulation outcome (success/failure, max clad temperature)
≅
DataObjects
(TimePointSet)

## Slide 7: ROMs: a Quick Introduction
Basically we are trying to reduce the complexity of the original model
Pros:
  Much faster computation of the output variable
Cons:
  Presence of error in the ROM computed values
≅
Original data (e.g., RELAP5)
ROM (e.g., quadratic regressor)

## Slide 8: Classes of ROMs
Model-Based
  Prediction is performed using a blend of interpolation and regression algorithms
  Examples:
    Gaussian Process Models (GPMs)
    Spline interpolator
Data-Based
  Prediction is performed by solely considering the input data by using data searching algorithms
  Examples:
    Nearest neighbor

## Slide 9: ROMs: Applications
Basic steps:
  Sample original model
  Train the ROM
  Perform desired analysis with the ROM
  instead of the original model
Range of applications:
  Uncertainty quantification / Sensitivity analysis
  Probabilistic Risk Analysis (PRA)
  Accelerator for stochastic analysis (adaptive sampling)
  Prediction models
Input x
Output y

## Slide 10: ROMs Available in RAVEN
  External libraries: Scikit-learn (http://scikit-learn.org)
  Open source machine learning library for Python
  Library for data mining and data analysis
  Built on NumPy and SciPy
Internally C++ developed libraries: CROW
  Generalized Polynomial Chaos (subject of a later presentation)
  Multi-dimensional interpolators
    ND Spline
    ND Inverse-Weight

## Slide 11: Scikit-Learn Library
Available:
  Classification: identifying to which category an object belongs
  Regression: predicting a continuous-valued attribute
  Data clustering: grouping similar objects into sets
  Dimensionality reduction: reducing the number of random variables
  Data pre-processing: feature extraction and normalization
Examples:
  Linear regression models
  Support Vector Machines
  Multi-Class classifiers
  Naïve Bayes
  Neighbors classifiers
  Tree classifiers
Notes: Add backup slides for some algorithms GPM and SVM

## Slide 12: Scikit-Learn Library
Classification
  Starting point: set of data points with labels
  [features, class]i
  Objective: identify which class a new point [features] belong
Clustering
  Starting point: set of data points
  [features]I
  Objective: group data points based on a specific distance metrics
Y
(μ1,σ12)
(μ2,σ22)
X
Notes: Add backup slides for some algorithms GPM and SVM

## Slide 13: Scikit-Learn Library
  Starting point: set of data points
  [features]i
Cardinality reduction
  Objective: identify the most relevant features that keep data points unique
  Outcome: Location of the points on the reduced space (e.g., line)
Regression
  Objective: estimate the relationships among variables via a statistical process
  Outcome: coefficients of the reduced space (e.g., m and c for linear interpolator )
Source: scikit-learn.org
Notes: Add backup slides for some algorithms GPM and SVM

## Slide 14: Multi-Dimensional Interpolators
CROW: Internally developed C++ library
Interpolation on any dimension
Response surface is created as an interpolation function given a set of data points defined on:
  Sparse grid
  Cartesian grid
Extension of the known 1-D interpolation schemes

## Slide 15: Multi-Dimensional Interpolators
Two classes of algorithms
  Inverse-Weight
    No interpolation kernel is defined
    Defined on sparse grid
  Multi-Dimensional Spline
    Defined on cartesian grid
    Based on multi-dimensional spline kernel
    Continuity of the derivative is preserved
where:

## Slide 16: RAVEN ensemble modeling

## Slide 17: Ensemble Model
A new model entity (e.g., class), named EnsembleModel, has been developed:
  Assemble multiple models of other categories, identifying the input/output connections and the order of execution
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 18
Model 1
Model N-1
Model N
Model 1
Model 2
Model 3
  Ensemble Model: Chain of Models
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 19
  Ensemble Model: Non Linear
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 20: RAVEN ensemble modeling: 3 simple examples

## Slide 21
1-Dimensional heat conduction transient (in a slab of thickness L=1 m):
  EM1, heat conduction partial differential equation:
  EM2, thermal conductivity (input of EM1) as function of the average temperature in the slab boundary conditions:
EM1
EM2
  Ensemble Model: Example 1

## Slide 22
1-Dimensional heat conduction transient (in a slab of thickness L=1 m):
  EM1, heat conduction partial differential equation:
  EM2, thermal conductivity (input of EM1) as function of the average temperature in the slab (solution):
EM1
EM2
  Ensemble Model: Example 2

## Slide 23
Also codes can be used in the Ensemble modeling.
  EM1: Code, Analytical Bateman
    Transmutation
  EM2: External Model, compute the sum of the final outcomes of EM1
EM1
EM2
  Ensemble Model: Example 3

## Slide 24: RAVEN Examples

## Slide 25: RAVEN examples: ROMs

## Slide 26: ROM Modeling Within RAVEN
All modeling steps that involve ROMs are available in RAVEN
  Create ROMs from a database
  Perform statistical analysis using ROMs

## Slide 27: Exercise 1: Create a ROM from a database

## Slide 28: Workflow
Sample model
ROM_example.xml
Create database
Train a ROM
Sample a ROM
Stat Analysis

## Slide 29: Sample a Model and Create a Database
Samplers
Models
Distributions
Steps
Databases
DataObjects
<Distributions>
<Normal name='normal_trunc'>
<mean>0.5</mean>
<sigma>0.1</sigma>
<lowerBound>0.0</lowerBound>
<upperBound>1.0</upperBound>
</Normal>
<Normal name='normal'>
<mean>2.0</mean>
<sigma>0.2</sigma>
</Normal>
<Uniform name='uniform'>
<upperBound>4.0</upperBound>
<lowerBound>1.0</lowerBound>
</Uniform>
</Distributions>
Truncation parameters
Input file name: sample_model.xml

## Slide 30: Sample a Model and Create a Database
Models
Distributions
<Models>
<ExternalModel name='PythonModule' subType=’’ ModuleToLoad='workshop_model’>
<variables>
x1,
x2,
x3,
y1,
y2,
y3,
y4,
y5
</variables>
</ExternalModel>
</Models>
Samplers
Steps
Databases
DataObjects
Input variables
Output variables
File name: workshop_model.py
Input file name: sample_Function.xml

## Slide 31: Sample a Model and Create a Database
Samplers
Distributions
<Samplers>
<Grid name='Grid_function'>
<variable name='x1' >
<distribution>normal_trunc</distribution>
<grid type='value’ construction='equal' steps='5'>0.0 1.0</grid>
</variable>
<variable name='x2' >
<distribution>normal</distribution>
<grid type='value’ construction='equal' steps='5'>1.5 2.5</grid>
</variable>
<variable name='x3' >
<distribution>uniform</distribution>
<grid type='value’ construction='equal' steps='5’>1.0 4.0</grid>
</variable>
</Grid>
</Samplers>
Models
Steps
Databases
DataObjects
<variable name>
<distribution>
<grid points>
Input file name: sample_Function.xml

## Slide 32: Sample a Model and Create a Database
Distributions
<Databases>
<HDF5 name='out_db'/>
</Databases>
<DataObjects>
<TimePointSet name='Data1'>
<Input>x1,x2,x3</Input>
<Output>OutputPlaceHolder</Output>
</TimePointSet>
<TimePointSet name='inputPlaceHolder'>
<Input>x1,x2,x3</Input>
<Output>y1,y2,y3,y4,y5</Output>
</TimePointSet>
</DataObjects>
Databases
DataObjects
Samplers
Models
Steps
<DataObjects>
<Inputs>
<Output>
Input file name: sample_Function.xml

## Slide 33: Sample a Model and Create a Database
Distributions
Steps
Samplers
Models
Databases
DataObjects
Step
Model file
Model info
Sampler
Database
DataObjects
Input file name: sample_Function.xml
<Steps>
<MultiRun name='FirstMRun'>
<Input class='DataObjects' type='TimePoint' >inputPlaceHolder</Input>
<Model class='Models' type='ExternalModel’>PythonModule</Model>
<Sampler class='Samplers' type='Grid' >Grid_function</Sampler>
<Output class='DataObjects’ type='TimePointSet’ >outGRID</Output>
<Output class='Databases' type='HDF5' >out_db</Output>
<Output class='OutStreamManager' type='Print' >out_dump</Output>
<Output class='OutStreamManager' type='Plot' >plotResponseFunction</Output>
</MultiRun>
</Steps>

## Slide 34: Workflow
Sample model Create database
Train a ROM
Sample ROM
sample_Function.xml
sample_ROM.xml

## Slide 35: Train and Sample a ROM
Samplers
Models
Distributions
Steps
Databases
DataObjects
<Distributions>
<Normal name='normal_trunc'>
<mean>0.5</mean>
<sigma>0.1</sigma>
<lowerBound>0.0</lowerBound>
<upperBound>1.0</upperBound>
</Normal>
<Normal name='normal'>
<mean>2.0</mean>
<sigma>0.2</sigma>
</Normal>
<Uniform name='uniform'>
<upperBound>4.0</upperBound>
<lowerBound>1.0</lowerBound>
</Uniform>
</Distributions>
Truncation parameters
Input file name: sample_ROM.xml

## Slide 36: Train and Sample a ROM
Models
Distributions
<Models>
<ROM name='ROM4' subType='NDinvDistWeight'>
<Features>x1,x2,x3</Features>
<Target>y4</Target>
<p>3</p>
</ROM>
</Models>
Samplers
Steps
Databases
DataObjects
Input file name: sample_ROM.xml
Multi-dimensional interpolator (CROW)

## Slide 37: Train and Sample a ROM
Samplers
Distributions
Models
Steps
Databases
DataObjects
<Samplers>
<Grid name=’Grid_ROM'>
<variable name='x1'>
<distribution>normal_trunc</distribution>
<grid type='value' construction='equal' steps='10’>0.0 1.0</grid>
</variable>
<variable name='x2’>
<distribution>normal</distribution>
<grid type='value' construction='equal' steps='10’>1.5 2.5</grid>
</variable>
<variable name='x3’>
<distribution>uniform</distribution>
<grid type='value' construction='equal' steps='10'>1.0 4.0</grid>
</variable>
</Grid>
</Samplers>
Finer grid
Input file name: sample_ROM.xml

## Slide 38: Train and Sample a ROM
Distributions
Databases
DataObjects
Samplers
Models
Steps
<Databases>
<HDF5 name='out_db' filename='out_db.h5' directory='path2DB/DBStorage/'/>
</Databases>
<DataObjects>
<TimePointSet name='outGRID_y4'>
<Input>x1,x2,x3</Input>
<Output>y4</Output>
</TimePointSet>
<TimePointSet name='outROM_y4'>
<Input>x1,x2,x3</Input>
<Output>y4</Output>
</TimePointSet>
<TimePointSet name='Data1'>
<Input>x1,x2,x3</Input>
<Output>OutputPlaceHolder</Output>
</TimePointSet>
</DataObjects>
Input file name: sample_ROM.xml
Database containing training dataset
Training DataObject
ROM generated DataObject

## Slide 39: Train and Sample a ROM
Distributions
<Steps>
<IOStep name='extract_data4'>
<Input class='Databases' type='HDF5' >out_db</Input>
<Output class='DataObjects' type='TimePointSet' >outGRID_y4</Output>
</IOStep>
<RomTrainer name='rom_trainer4'>
<Input class='DataObjects' type='TimePointSet' >outGRID_y4</Input>
<Output class='Models' type='ROM' >ROM4</Output>
</RomTrainer>
<MultiRun name=’RunRom4'>
<Input class='DataObjects’ type='TimePointSet’ >Data1</Input>
<Model class='Models' type=’ROM’ >ROM4</Model>
<Sampler class='Samplers' type='Grid' >Grid_ROM</Sampler>
<Output class='DataObjects’ type='TimePointSet' >outROM_y4</Output>
</MultiRun>
</Steps>
Steps
Samplers
Models
Databases
DataObjects
Input file name: sample_ROM.xml

## Slide 40: Train and Sample a ROM
Inputs: x1, x2, x3
Output: y3

## Slide 41: Thank you Questions?