## Slide 1: RAVEN Introduction
Presenter: Cristian Rabiti

## Slide 2: RAVEN Structure

## Slide 3: Capabilities vs. Needs
Algorithms | User Cases |  |  |  |  | 
 | Uncertainty Quantification | Risk Analysis | Risk Management | Validation | Experiment design | Optimization
Distribution | Yes | Yes | Yes | Yes | Yes | Yes
Sampling | Yes | Yes | Yes | Yes | Yes | Yes
Surrogate Models | Yes | Yes | Yes | Yes | Yes | Yes
Statistical post processing | Yes | Yes | Yes | Yes | Yes | Yes
Reliability Surface |  | Yes | Yes |  |  | 
Data mining |  | Yes | Yes |  |  | 
Analytical distribution comparison (ongoing) |  |  |  | Yes | Yes | 
Minimization Algorithms (ongoing) |  |  | Yes |  | Yes | Yes

## Slide 4: Distributions
Distribution describe the statistical behavior of input parameters

## Slide 5: Standard Distributions
Most common used 1D distributions

## Slide 6: N-Dimensional Distributions (Unique capabilities)
Import from file for custom N-dimensional distributions:
  N-dimensional splines on Cartesian grids
  Inverse weight interpolation
  Micro sphere interpolation
Sampling of N-dimensional distributions by not biased random inversion

## Slide 7: Distribution Input
<Distributions>
<Normal name='x_distrib'>
<mean>2</mean>
<sigma>0.2</sigma>
</Normal>
</Distributions>
Models
Files
Run Info
Steps
Distribution
Functions
Samplers
Database

## Slide 8: Sampler
Samplers determine the strategy for exploring the input space

## Slide 9: Samplers (non-Adaptive)
RAVEN supports many non-adaptive samplers
Monte Carlo
Grids:
  equal-spaced in probability
  equal-spaced in value
  mixed (probability, custom, value)
  Custom (used provided values/probability)
Stratified (LHS type)
  equal-spaced in probability
  equal-spaced in value
  mixed (probability, custom, value)
  Custom (used provided values/probability)
Generalized stochastic collocation polynomial chaos
A different sampling strategies can be associated to each variable separately

## Slide 10: Samplers (non-Adaptive) Cont.
Factorial Designs:
  General Full Factorial (grid)
  2-Level Fractional-Factorial
  Plackett-Burman
Response Surface Designs:
  Box-Behnken
  Central Composite
Box-Behnken
Central Composite

## Slide 11: Dynamic Event Trees (DET)
Chart: 
| 200.0 | 220.0 | 240.0 | 260.0 | 280.0 | 300.0 | 320.0 | 340.0 | 360.0 | 380.0 | 400.0
CDF | 0.0062097 | 0.02275 | 0.066807 | 0.15866 | 0.30854 | 0.5 | 0.69146 | 0.84134 | 0.93319 | 0.97725 | 0.99379
Chart: 
| 200.0 | 220.0 | 240.0 | 260.0 | 280.0 | 300.0 | 320.0 | 340.0 | 360.0 | 380.0 | 400.0
Pb | 0.043821 | 0.13498 | 0.32379 | 0.60493 | 0.88016 | 0.99736 | 0.88016 | 0.60493 | 0.32379 | 0.13498 | 0.043821
Pipe failure pressure
Pipe failure pressure
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
pressure | 200 | 220 | 280 | 190.4 | 250 | 270 | 290 | 320 | 0 | 0
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
 | 200 | 220 | 280 | 190.4 | 250 | 270 | 0 | 0 | 0 | 0
Failure @66% CDF
Failure @33% CDF
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
 | 200 | 220 | 280 | 190.4 | 250 | 270 | 290 | 320 | 330 | 340
Probability
Cumulative Distribution Function (CDF)
Time
Time
Time
Pressure
Pressure
Pressure
Stochastic system could not be fully controlled by the initial condition
Sampling is decided beforehand for “control variables”
the corresponding simulation is run only if the physics triggers the control variable
DET can be used in a mixed fashion with any of the other sampler
DET available with RELAP5-3D, MAAP, RELAP-7

## Slide 12: Adaptive Sampler: Reliability Surfaces Finder
High Risk Direction
Risk Neutral Direction
Trying to avoid high temperature regions
Excessive Temperature Region
The sampler seeks to determine a region in the input parameter space for which a given condition is satisfied
Used to determine operative safe regions
Performance optimization

## Slide 13: Adaptive Stochastic Polynomials
Valuable when the parametric space is <10-15 variables
Selectively choose the sampling points to construct a polynomial representation of the system response
The plots shows how many evaluations are necessary to assess the mean of a variable depending from five stochastic parameters
Monte Carlo
Adaptive

## Slide 14: Input Sampler
<Samplers>
<MonteCarlo name='MCsampler'>
<samplerInit><limit>5000</limit></samplerInit>
  <variable name='x’>
  <distribution>x_distrib</distribution>
  </variable>
  </MonteCarlo>
<Grid name=’GridSampler’>
<variable name=‘x1’>
<distribution>x1_distrib</distribution>
<grid type=‘CDF’ construction=‘equal’ steps=’10’>0.0 1.0</grid>
</variable>
<variable name=‘x2’>
<distribution>x2_distrib</distribution>
<grid type=‘value’ construction=‘equal’ steps=‘8’>0.1 0.9</grid>
</variable>
</Grid>
  </Samplers>
Models
Files
Run Info
Steps
Distribution
Functions
Samplers
Database

## Slide 15: Queuing
Queuing strategies is used to take advantage of modern high performance computing

## Slide 16: Parallel Environment
RAVEN
JobHandler
Job 1
Job 2
Job ...
Job N
Batch Size
MPI 1
MPI 2
MPI ..
MPI M
Thread 1
Thread 2
Thread ..
Thread J
Modern codes are already parallel using MPI and multithreading
RAVEN manages concurrent runs of already parallel codes by sub-process (single nodes) or interfacing with the queuing software present in the environment (PBS professional implemented, API available for other software)

## Slide 17: Input: Step and RunInfo
<Runinfo>
<WorkingDir>./myDir</WorkingDir>
<Sequence>runMC</Sequence>
<batchSize>10</batchSize>
</Runinfo>
<Steps>
<MultiRun name=‘runMC’>
<Input class=‘Files’ type=‘’ >inputFile.i</Input>
<Model class=‘Models’ type=‘Code’ >RELAP5-3D</Model>
<Sampler class=‘Samplers’ type=‘MonteCarlo’>MCsampler</Sampler>
<Output class=‘DataObjects’ type=‘PointSet’ >outMC</Output>
</MultiRun>
</Steps>
Models
Files
Run Info
Steps
Distribution
Functions
Samplers
Database

## Slide 18: Models API
Model APIs is the way in which RAVEN access a physical model

## Slide 19: Models
RAVEN support three different models:
ROM (Reduced Order Models). This type of models are constitute by already trained supervised learning algorithms (RAVEN can use data sets for their training)
External Models. External models are made of python code that use directly the “model” class
External codes. These are classical third parties codes. The API requires the implementation of writing/reading to/from the input/output files

## Slide 20: Available ROMs
Nearest neighbor (KD-Tree based)
Support vector machine:
  Polynomial kernel
  Gaussian Kernels
  Radial basis functions
Micro Sphere
Inverse Weight
N-Dimensional spline
Gaussian process
Polynomial (stochastic and not)
Linear regressors
Many more (http://scikit-learn.org/stable/supervised_learning.html)
Ensemble models

## Slide 21: Model APIs
Base Model Class
ROM: Supervised Learning algorithms
ROM API. This API is build to match the standard interface to use the supervised algorithms of the scikit-learning library
External Models
The model in python is directly callable form RAVEN
External Code
Code API. This API requires the capability to write code input files and read output files. A generic implementation using wild card is available
Generic interface
Relap5-3D
MAAP
Melcor
MOOSE based applications

## Slide 22: Ensemble model
Multiple “models” can be assembled together and treated as a single one
Models can be completely heterogeneous (code, external models, ROM)
RAVEN acts as a hub for the information exchange
Information passed between “models” could be:
  Set of lump values
  Set of time series (being currently finalized)
Model
Model
Model
Ensemble model
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 23
<Models>
<ExternalModel name=‘PythonModule’ subType=‘’ ModuleToLoad=‘./externalModel’>
<variables>x,y</variables>
</ExternalModel>
</Models>
Input: Models
Models
Files
Run Info
Steps
Distribution
Functions
Samplers
Database

## Slide 24: Data Structure
RAVEN has its own internal data structure but also used HDF5 and CSV

## Slide 25
<DataObjects>
<PointSet name=‘outSampler’>
<Input>x</Input>
<Output>y</Output>
</PointSet>
</DataObjects>
<Databases>
<HDF5 name='out_ROM4_db’ readMode =‘overwrite’ />
<HDF5 name='out_ROM5_db’ readMode =‘overwrite’ directory='/pathToDatabase/’/>
<HDF5 name='out_db' readMode =‘read’ directory='/pathToDatabase/'/>
</Databases>
Input: Data
Database that is going to be created
Existing database that is going to be retrieved
Models
Files
Run Info
Steps
Distribution
Functions
Samplers
Database

## Slide 26: Post Processing
Interpretation of large data is a new challenge in large probabilistic analysis

## Slide 27: Statistical Post Processing
Statistical characterization of the output (uncertainty propagation)
Mean
Sigma
Skewness (asymmetry)
Kurtosis (more/less peaked than a standard normal)
Input/output relationship (ranking/sensitivity)
Correlation matrix
Covariance matrix
Sensitivity matrix (multidimensional linear regression)
Normalized sensitivity matrix (% change of the response / % change in the answer)

## Slide 28: Classical Data Mining
RAVEN gives access to several data mining algorithms for data post-processing via implementation of APIs between RAVEN and Scikit-learn*
Cardinality Reduction algorithms aim to recognize commonalities among the data - Clustering, Gaussian Mixture Models, etc.
Dimensionality Reduction algorithms are used to reduce the number of degrees of freedom in the data under consideration – Manifold Learning, Decomposing Signals in Components, etc.
RAVEN extends all the data mining algorithms to perform time dependent data mining
*http://scikit-learn.org

## Slide 29: Input: Basic Statistics
<Models>
<PostProcessor name='StatisticsOutput’ subType='BasicStatistics’>
<what>all</what>
<parameters>y1,y2,y3,y4,y5</parameters>
</PostProcessor>
</Models>
<Steps>
<PostProcess name='PP'>
<Input class='DataObjects’ type=’PointSet’ >outMC</Input>
<Model class='Models' type='PostProcessor’>StatisticsOutput</Model>
<Output class='Files' type='' >output_basicStatistics.csv</Output>
</PostProcess>
</Steps>
Models
Files
Run Info
Steps
Distribution
Functions
Samplers
Database

## Slide 30
Examples

## Slide 31: Probabilistic Analysis Results
The following table summarizes the results obtained with different sampling methodologies. Overall we obtained a good agreement
Sampler | Settings | Failure Probability (-)
Monte Carlo | 1224 runs | 1.31E-2
Grid Sampler | Equally value spaced 6x6x6x6= 1296 | 1.33E-2
Latin Hyper Cube | 1224 equally probability spaced | 1.34E-2
Monte Carlo
Grid
LHS

## Slide 32: MAAP
Dynamic Event tree coupling available with MAAP
126 branches simulated
54 completed histories
7 out of 54 histories ends due to the occurrence of “core uncovery”
“Core uncovery time” ranges from 5257 s to 12853 s
  Trajectories of the system evolution with respect different figure of merits: mass of water in the accumulators tanks, primary system pressure, steam generator 1 pressure, collapsed water level into the core

## Slide 33: Uncertainty Quantification
Demo: BWR Station Black Out analysis
Code: RELAP5-3D (10,000 runs)
Sampled variables:
  Elapsed time before Diesel Generation loos
  Diesel Down time
  Power Level
Clad Temperature (system Output):
Entry | Monte Carlo
Mean: | 2.32E+03
Sigma: | 9.05E+02
Kurtosis: | -1.54E+00
Median: | 3.09E+03
Skewness: | -5.25E-01

## Slide 34: Risk Management: Reliability Surface
Safe Region
Failure Region
Seeking the combination of parameters (axis) that allows not to exceed the maximum clad temperature

## Slide 35: Workflows
Sampler
+
Distributions
Model (code)
Post Processing
Data Base
Model (code)
ROM Training
Sampler
+
Distributions
Post Processing
Simulation 1
Simulation 2

## Slide 36: Comparison vs ROM
Statistical figures for max clad temperature:
Entry | Original | Surrogate
Mean: | 2.3296E+03 | 2.3103E+03
Sigma: | 9.0559E+02 | 8.4599E+02
Kurtosis: | -1.547E+00 | -1.4497E+00
Median: | 3.092E+03 | 2.683E+03
Skewness: | -5.256E-01 | -5.0662E-01
Failure Pb | 60.99% | 60.82%
The matching of the results between the Monte Carlo Sampling on the RELAP5-3D code and the build surrogate confirm the good training set
New input distributions could be tested without re-running the original code but using the ROM

## Slide 37: Time Dependent Statistics: Fuel Performance
  95% percentile
  Mean
  Median
  5% percentile
  Max hoop stress during transient as a function of burn up

## Slide 38: Time Dependent Relational Analysis
  The correlation analysis reveals how much each input is linearly related to the input space
  Changes in the correlation coefficient usually indicate a change in the dominating physics

## Slide 39: Clustering to Analyze Behavior Drivers (Fuel Performance
Input Parameters
Power scaling factor of the core
Scaling factor of the grain size in the fuel microstructure
Thermal expansion coefficient of the fuel
Output Parameters
Average Clad Temperature
Average Interior Temperature
Fission Gas Released
  Clustering structure in the output space when projected in the input space reveals that the power is the discriminant driver of the cluster structure

## Slide 40: Stochastic Optimization
  Optimization of electricity supply mix under stochastic wind supply

## Slide 41: How Can I use it (Risk Management)?
Create an ensemble model using several codes
Compute the failure probability of the ensemble system using the limit surface
Good enough?
  Yes, stop
  No, go on
Cluster the system evolution to identify if there where cliff edge effects
  Yes: determine the discriminant point and improve design
  No: perform sensitivity analysis: move the mean values or decrease uncertainty on the input space

## Slide 42: How Can I use it (Risk Differential Analysis)?
Run dense sampling
Train a ROM
Sample the ROM changing failure probability of each component (from 100% failure rate to 0%) to evaluate the single contribution and the global impact

## Slide 43: Design of Experiment
Model the experiment
Run the experiments with input uncertainties
Use as figure of merits the experimental readings
Use dimensionality reduction in the output space (experimental readings) to determine redundancy in the experimental sensors (remove redundant readings –save money-)
Analyze the sensitivity of the experimental reading to variation in the input space to:
  Eliminate the one too sensible to not controllable uncertainties
  Eliminate the one that are not sensitive to the model parameters to be validated

## Slide 44: RAVEN Status
Code available in beta release
User manual
Theory/guidelines manual
Possible open source coming soon
Supported platforms:
  Linux
  Mac OS
  Windows