## Slide 1: Overview
RAVEN workshop
PSA 2015 - April 26th 2015, Sun Valley (ID)
C. Rabiti, A. Alfonsi, S. Sen, D. Maljovec, P. Talbot, R. Kinoshita, D. Mandelli, J. Cogliati

## Slide 2
RAVEN
Risk Analysis Virtual ENvironment

## Slide 3: Project Background
RAVEN started in early 2012
  Supported by the Nuclear Energy Advanced Simulation (NEAMS) program
  The Light Water Reactor Sustainability (LWRS) program is the major customer and supporter
The overall goal was to have a tool to enable Risk Informed Safety Margin Characterization (RISMC)
  Evaluating risk (uncertainty propagation)
  Understanding risk (limit surface, ranking, sensitivity, data mining)
  Mitigating risk (optimization)

## Slide 4: For Which Type of Systems
Uncertainty in initial condition
Probability distribution of the final status
Uncertainty in system response
Uncertainty in initial and boundary condition
Uncertainty in model parameters
Stochastic events
Possibly dealing with discrete variable
Highly non linear systems

## Slide 5: Which Tools
Risk Management
Risk Evaluation
Risk Analysis
Risk Mitigation
Probability
Consequence
Probability functions
Sampling
Ranking
Sensitivity
Limit Surface
Data Mining
Optimization
Surrogate Models
Dynamic Event Trees
Adaptive Dynamic Event Trees

## Slide 6: How
Storage
Output Reader
Run manager
Sampling
Distribution
Variable ID
Code Input
RAVEN could interact with a physical model by:
  Wrapping the code simulating the physical moment
  Exchanging information at each time step (only for RELAP-7 and MOOSE based application soon)
  Leveraging already existing control logic structure in the code (e.g. RELAP5-3D for Dynamic Event Trees)
RAVEN Input File
RAVEN
Input syntax
User Built Interface
Values
New
Input
New
Output
Data

## Slide 7: Parallel Environment
Sampling is a very expensive computational operation
Modern codes are already parallel using MPI and multithreading
RAVEN manages concurrent runs of already parallel codes
RAVEN
JobHandler
Job 1
Job 2
Job ...
Job N
Batch Size
MPI 1
MPI 2
MPI ..
MPI M
Thread 1
Thread 2
Thread ..
Thread J

## Slide 8: The Building Blocks
RAVEN is organized in a modular fashion where “entities” can be used to construct the sought workflow
The building blocks are:
  Distributions: describe the probabilistic behavior of variables
  Samplers: associate the distribution with a variable and a sampling strategy
  Models: represent the system to be explored or more generally an input output relationship
The actions (Steps):
  MultiRun/Run: feeds an input to a model to retrieve an output, if a sampler is present the model is sampled according
  Postprocessor: investigate outputs to determine their statistical characterization and relate the output to the input
  IO: export import data where the output are stored

## Slide 9: Probability Distribution Functions (1D)
Most common used 1D distributions (Boost)

## Slide 10: Probability Distribution Functions (ND)
Multivariate distributions appear in many practical problems
They are challenging from two points of view:
  Construction and evaluation
  Sampling (they are not invertible)
RAVEN manages
  Multivariate normal:
  Custom, user-provided distributions (supplied as a file of evaluated points)

## Slide 11: Samplers (non-Adaptive)
Choose how to sample the input (parametric) space:
  Impacts how effectively the input space is explored
  Determines the probability associated with each realization of the output
RAVEN supports many non-adaptive samplers
  Monte Carlo
  Grid
    Equal-spaced in probability
    Equal-spaced in value
    Mixed
    Custom
  Stratified (LHS type)
    Equal-spaced in probability
    Equal-spaced in value
    Mixed
    Custom

## Slide 12: Samplers (non-Adaptive) Cont.
Factorial Designs:
  General Full Factorial (grid)
  2-Level Fractional-Factorial
  Plackett-Burman
Response Surface Designs:
  Box-Behnken
  Central Composite
Box-Behnken
Central Composite
High density sampler focused on full coverage of the input space (highly discontinuous and nonlinear response, low dimensionality)

## Slide 13: Spatial Distribution Examples
Monte Carlo (300 points)
Grid (1764 points)
Latin Hypercube (100 points)

## Slide 14: Dynamic Event Tree
Chart: 
| 200.0 | 220.0 | 240.0 | 260.0 | 280.0 | 300.0 | 320.0 | 340.0 | 360.0 | 380.0 | 400.0
CDF | 0.0062097 | 0.02275 | 0.066807 | 0.15866 | 0.30854 | 0.5 | 0.69146 | 0.84134 | 0.93319 | 0.97725 | 0.99379
Chart: 
| 200.0 | 220.0 | 240.0 | 260.0 | 280.0 | 300.0 | 320.0 | 340.0 | 360.0 | 380.0 | 400.0
Pb | 0.043821 | 0.13498 | 0.32379 | 0.60493 | 0.88016 | 0.99736 | 0.88016 | 0.60493 | 0.32379 | 0.13498 | 0.043821
Pipe failure pressure
Pipe failure pressure
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
pressure | 200 | 220 | 280 | 190.4 | 250 | 270 | 290 | 320 | 0 | 0
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
 | 200 | 220 | 280 | 190.4 | 250 | 270 | 0 | 0 | 0 | 0
Failure @66% CDF
Failure @33% CDF
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
 | 200 | 220 | 280 | 190.4 | 250 | 270 | 290 | 320 | 330 | 340
Probability
Cumulative Distribution Function (CDF)
Time
Time
Time
Pressure
Pressure
Pressure
Intrinsically-stochastic systems cannot be controlled by the initial condition

## Slide 15: Dynamic Event Tree (DET) Example
Clad Temperature [K]
Time [s]
All the tree branches are assembled to reproduce the full evolution
* = system success
* = system failure

## Slide 16: DET Follows Failure Patterns
DG Recovery Time [s]
Clad Failure Temperature [K]
Increase the delay in the recovery of the DG until…
The first clad failure threshold is reached
* = system success
* = system failure
The consideration of uncertainty on clad failure temperature leads to a natural refinement of the analysis around the failure prone input space
Clad branching:
DG branching:

## Slide 17: Models
At the software level, models relate input to output
It might be more convenient to think about a model as software simulating a physical system
Within this context the following models are available:
  Code: an external code that RAVEN can inquire via properly-built interfaces to manage input and output
  External model: a numerical implementation of a physical model that is interfaced to RAVEN directly (no file exchange) using RAVEN’s API
  An internally generated surrogate models (ROM)

## Slide 18: Data
RAVEN posses four main data type
Time Point Set
Time Point
Input Set
Output Set
Histories
History
Input Set
Time series
Many
Many
For a set of the input parameters ... the corresponding figures of merit

## Slide 19: Statistical Post Processing
Statistical characterization of the output (uncertainty propagation)
Mean
Sigma
Skewness (asymmetry)
Kurtosis (more/less peaked than a standard normal)
Input/output relationship (ranking/sensitivity)
Correlation matrix
Covariance matrix
Sensitivity matrix (multidimensional linear regression)
Normalized sensitivity matrix (% change of the response / % change in the answer)

## Slide 20: Input/Output Relationship
 | Input Parameters |  | Output FOM | 
Input Parameters |  |  |  | 
Output FOM |  |  |  | 
Input Correlation
Input to Output Correlation
Output Correlation
Correlation matrix
Covariance matrix
Sensitivity matrix
Normalized sensitivity matrix

## Slide 21: Advanced Post Processing
RAVEN gives access to several data mining algorithms for data post-processing via implementation of APIs between RAVEN and Scikit-learn*
Cardinality Reduction algorithms aim to recognize commonalities among the data - Clustering, Gaussian Mixture Models, etc.
Dimensionality Reduction algorithms are used to reduce the number of degrees of freedom in the data under consideration – Manifold Learning, Decomposing Signals in Components, etc.
In principle data mining makes no distinction between input and output
*http://scikit-learn.org

## Slide 22: Application to BISON Fuel Analysis
Power Scale Factor
Grain Radius Scale Factor
Mid-PLane Vonmises Stress
~17,000 simulations, 3 input parameters
power_scalef | Power scaling factor of the core
grainradius_rscalef | Scaling factor of the grain size in the fuel microstructure
thermal_expansion | Thermal expansion coefficient of the fuel
Average Clad Temperature
Average Interior Temperature
Fission Gas Released
Output Space
Input - Output Space
K-Means algorithm (Lloyd’s algorithm)
No. Clusters: 2
Notes: Kmeans Algorithm: clusters data by trying to separate samples in n (number of clusters (given by user)) groups of equal variance, minimizing the criterion known as inertia. It scales well to large number of samples, and has been widely used in different fields.
Inertia: the within-cluster sum of squares criterion, can be recognized as a measure of how internally coherent clusters are.
Silhouette Coefficient: Silhouette refers to a method of interpretation and validation of clusters of data. The technique provides a succinct graphical representation of how well each object lies within its cluster.
The best value is 1 and the worst value is -1. Values near 0 indicate overlapping clusters. Negative values generally indicate that a sample has been assigned to the wrong cluster, as a different cluster is more similar.

## Slide 23: Simple Workflow
Definition of the distributions to be used
Definition of the sampler
  Association of variable name(s) with distribution(s)
  Choice of a sampling strategy
Definition of the data structure(s) for internal storage
Evaluation step
  The distributions are sampled according to the sampler
  The variables are associated to the values
  The model is executed as many times as the sampler requires
  The inputs and corresponding outputs are stored in the data structure(s)
Post-processing
  The data is analyzed according to requested type of post-processing
I/O
  Data is saved for further analysis

## Slide 24: Reduced Order Models (ROM)/Surrogate Models
Not for all possible inputs, but for a range of possibilities…
Not for all possible geometries, but for a parametric range…
Not to represent all outputs, but for some of the outputs…
It is possible to:
-Build a set of equations of faster solution with respect to the original set
-Increase the prediction capabilities by further training

## Slide 25: Using Surrogate Models
Sampler
+
Distributions
Model (Code)
Post Processing
Data Base
Model
ROM Training
Sampler
+
Distributions
Post Processing
Simulation 1
Simulation 2

## Slide 26: Available Surrogate Models
The surrogate models available are:
  Supervised algorithms available from scikit-learn
    SVMs
    Nearest neighbor
    Gaussian Process
    Etc…
  Inverse weight
  ND spline (only regular Cartesian grids)
  Generalized Polynomial Chaos Expansion
RAVEN has an API to implement your own surrogate model

## Slide 27: Reliability Analysis (Limit Surface)
High Risk Direction
Risk Neutral Direction
Trying to avoid high temperature regions
System response depends on many variables but often what matters are a few figures of merit
What is the probability of exceeding the threshold?
Which parameter is the most influential?
Which uncertainties affect my margins the most?
Excessive Temperature Region

## Slide 28: Limit Surface Example
Safe Region
Failure Region

## Slide 29: Adaptive Dynamic Event Tree (A-DET)
The DET’s intrinsic characteristic of following failure patterns provides a more effective training set than other random sampling approaches
The next point is mapped into the database of already-executed branches
Only the last part of the simulation is run

## Slide 30: Dynamic Event Tree Demo
Training
Convergence
No density increase

## Slide 31: Databases and IO
RAVEN posses the capability to dump the internal data in:
  HDF5 databases
  CSV files (raw output plus metadata)
Both HDF5 and CSV could be used to recreate the data set during sub sequential simulations

## Slide 32: Stochastic Polynomials
It is a special type of surrogate model
It requires a specific sampling strategy
Some of the information of statistical relevance are analytical from the coefficients of the surrogate model
Polynomial Representation
  Given a quantity of interest:
  Represent as combination of polynomials:
    Simpler to evaluate
    Easy to get statistical moments
    Less effort and more accurate than Monte Carlo

## Slide 33: Stochastic Collocation
Effectiveness depends on:
  Regularity of quantity of interest
  Polynomial expansion order
  Polynomial combination indices
  Sparse Grid quadrature types (Gauss, Clenshaw)
  Number of uncertain inputs
Tensor Product: Overkill
Total Degree: For Analytic Uncertainty
Hyperbolic Cross: For Irregular Uncertainty

## Slide 34: Application of Stochastic Polynomials
Statistic | Mean (x10^8) | Std. Dev. | Failure Pb | Solves | Err Stdev *Runs
BISON MC (reference) | 5.84360195 | 4.75237678 | 0.0986 | 10000 | 
J_HC2 (error) | 5.13E-06 | 8.91E-03 | 7.61E-02 | 7 | 0.0624
J_HC4 (error) | -3.48E-05 | 9.95E-03 | 7.10E-02 | 31 | 0.3084
J_HC8 (error) | -2.35E-05 | 9.63E-03 | 7.91E-02 | 153 | 1.4736
J_TD2 (error) | -2.60E-05 | 6.41E-01 | 8.01E-02 | 25 | 16.0187
J_TD4 (error) | -2.93E-05 | 9.64E-03 | 7.61E-02 | 165 | 1.5899
J_TD8 (error) | -1.92E-05 | 9.19E-03 | 7.71E-02 | 2097 | 19.2691
L_HC2 (error) | 1.70E-04 | -6.88E-02 | -1.38E-01 | 7 | 0.4818
L_HC4 (error) | 3.38E-05 | -1.91E-02 | 1.38E-01 | 31 | 0.593
L_HC8 (error) | 1.71E-05 | 3.32E-03 | 8.72E-02 | 153 | 0.5087
L_TD2 (error) | 1.52E-04 | -6.90E-02 | 8.82E-02 | 25 | 1.7261
L_TD4 (error) | 1.53E-05 | -1.87E-02 | 1.20E-01 | 165 | 3.0929
L_TD8 (error) | -1.28E-05 | 1.35E-03 | 7.10E-02 | 2097 | 2.8219

## Slide 35: Structured Sensitivity Analysis via Topological Decomposition
(a) Decompose the domain based on gradient flow from/to local minima/maxima
(b) Fit a linear regressor to each local segment of the data

## Slide 36: Application to BISON Fuel Analysis
~17,000 simulations
3 input parameters:
  power_scalef = Power scaling factor of the core
  grainradius_rscalef = Scaling factor of the grain size in the fuel microstructure
  thermal_expansion = Thermal expansion coefficient of the fuel
Response value: Midplane Von Mises Stress
Goal: Determine most sensitive parameters within each subset of the domain

## Slide 37: How to get the Code
RAVEN is available for free to:
  University (no commercial use allowed)
  DOE
RAVEN license is worded such that INL retains the intellectual property of any new developments from third parties
We are currently talking with commercial entities and we would be interested in supporting commercial applications
Contact: cristian.rabiti@inl.gov, beth.jagger@inl.gov