## Slide 1
Sparse Sensing

## Slide 2: DT Capabilities
1. Physical Space
2. Digital/Virtual Space
3. Data Space
(Prediction/Monitoring/Control)
4. Services Space
(ASI, P&ID, BOM, Actuators)
(CAD/GUIs/Analytics)
(Storage, Connectivity, IIoT)
Reliability Analysis
[Un]supervised Learning
Sparse Learning
Reinforcement Learning
VV&Q
Optimization
System Optimization
Anomaly detection
Economical Modeling
Model/data assimilation/adjustment
Cyber Resilience and DSP/TSA
Model Predictive Control (MPC)
SPSL
SR2ML
ORNL AGING
SRAW
SONAR
VISP
ANL FARM
LOGOS
TEAL
HERON
Core Capability
https://github.com/idaholab/raven/wiki
RAVEN Plugin
Future capability

## Slide 3: Unique Capability: Sparse Sensing
Risk/
Reliability Analysis
ML/AI
Sparse Learning
Reinforcement Learning
Validation, Verification and Qualification (VVQ)
Optimization
System Optimization
Anomaly detection
Economical Modeling
Model/data assimilationadjustment
Cyber Resilience and DSP/TSA
Model Predictive Control (MPC)
Sparse Learning
SPSL
Problem Statement: Enable sparse sensing and sparse learning in nuclear digital twins through reconstruction of reactor core flow fields, using optimal sensor placement with spatial constraints
Opti-TWIST Capsule
n = All possible sensor locations
r = Selected sensors
= Constrained locations
s = Maximum sensors in Constrained region

## Slide 4: OPTI-TWIST Prototype

## Slide 5: Data warehouse
1. Physical Space
2. Digital/Virtual Space
3. Data Space
(Prediction/Monitoring/Control)
4. Services Space
(ASI, P&ID, BOM, Actuators)
(CAD/GUIs/Analytics)
(Storage, Connectivity, IIoT)

## Slide 6: Data warehouse
1. Physical Space
2. Digital/Virtual Space
3. Data Space
(Prediction/Monitoring/Control)
4. Services Space
(ASI, P&ID, BOM, Actuators)
(CAD/GUIs/Analytics)
(Storage, Connectivity, IIoT)

## Slide 7: Model Calibration Experiment(s)
Image courtesy : Idaho National Laboratory (INL)

## Slide 8: Uncertainty Quantification – Reconstruction and Heatmaps

## Slide 9: Conclusions
Reconstruction error decreases with more optimized sensors (unconstrained or constrained)
Random placements still suffer from high error even with additional sensors.
Implemented in RAVEN and PySensors (Open-source softwares)

## Slide 10: Hands-on Session

## Slide 11: Hands-on session
11
Opti-Twist unconstrained reconstruction:
Input features: x, y, temperature (Temperature is the state variable, that’s why for now it is among the features and targets)
target: .
Please use 4 modes, SVD basis, and 4 sensors

## Slide 12: testSPSLOptiTwist.xml
12
Procedure: change directory (cd) to: `cd ~/projects/raven/doc/workshop/SparseSensing/exercises` (For windows you might need to add double quotes)
Add the path to the needed files in the <Files> node.
Provide the input names in the LoadCSV <IOStep>
Complete the Model in the <PostProcess> step
Complete the <Models> block:
  Goal of the analysis: Is it reconstruction or classification?
  features: provide all the features used in the training. Refer to the csv files
  nModes, and nSensors should be set to 4. Please try different values, what happens if they are not equal?
Run the raven input: raven_framework testSPSLOptiTwist.xml

## Slide 13: RAVEN RESULTS
13

## Slide 14: Industrial App. 1 - Nuclear Fuel Capsules
Goal 1 : Optimize height (Z-axis) at which thermocouples should be placed inside the fuel to reconstruct fuel temperature profile.
Goal 2 : Choose best thermocouple locations on the graphite holder from all the green holes shown in Figure 1 to reconstruct the fuel temperature profile.
Figure 1 : Top view of Graphite Holder 5 with thermocouple locations.
Figure 2 : Graphite Holder 5 with fuel in 3D.

## Slide 15: TRISO Fuel Irradiation Experiment
Constrained
Unconstrained
Random
Sensor | X | Y | Z
0 | 0.892 | 0.892 | 12.3080
1 | -1.081 | 0.000 | 14.1535
2 | -1.088 | -0.438 | 9.8000
Sensor | X | Y | Z
0 | -0.638 | 0.005 | 9.000
1 | -0.302 | -0.781 | 11.154
2 | 0.306 | 0.783 | 14.167
Sensor | X | Y | Z
0 | -1.050 | 0.110 | 11.346
1 | 0.857 | 0.252 | 14.000
2 | 0.615 | 0.892 | 10.962

## Slide 16: TRISO Fuel Temperature Reconstruction
(a-c) Temperature profile reconstructions (d-e) Relative reconstruction errors. Unconstrained optimization leads to a maximum reconstruction error of ε = 0.75% (a,d), while introduction constraints results in ε = 1% (b,e). Random sensor placement (c,f) results in inaccurate reconstructions ε = 25% compared to that of optimized sensor locations

## Slide 17: Industrial Application 2: Sensor Placement for Steam generator Design
Baffles = Constraints

## Slide 18: 1D Steam Generator Temperature Modeling Results
a) Constrained sensor reconstruction ε = 0.9%
(b) Max reconstruction error over all test samples is 0.9%
(c) High uncertainty in temperature transition zones
Secondary side temperature profile reconstructed from 3 constrained sensors results in a maximum reconstruction error of 0.9 % over all test samples (a,b) and the maximum uncertainty in reconstruction for noisy sensor measurements is 0.01 °F (c).

## Slide 19: 1D Steam Generator Heat Flux Modeling Results
The leading three POD modes of secondary side temperature capture 99 % of energy content and provide accurate reconstructions of temperature fields. The first POD mode captures the secondary side temperature profile whereas the 3rd POD mode captures variation in the heat flux that cause changes in temperature along the normalized z coordinates in the steam generator
Heat Flux inferred from reconstructed temperature measurements

## Slide 20: Future Work
Optimal sensor placement for multi-class classification, (predicting which accident scenario (Loss of Coolant Accident (LOCA), loss of power, etc.)
Using Mutual Information and Entropy-based metrics for sensor placement.
Comparing sensor selection to other feature selection algorithms and utilize them to improve selection of sensors.
Measuring a certain field of interest (e.g., temperature) and inferring another field of interest (e.g., velocity).
Anomaly detection
Tensor decomposition instead of Singular value decomposition (SVD) when we have time and samples.
Implementing constrained sensor placement in RAVEN.
Confusion Matrix

## Slide 21
Thanks for attention!

## Slide 22
Krithika Manohar, J Nathan Kutz, and Steven L Brunton. “Optimal sensor and actuator selection using balanced model reduction”. In: IEEE Transactions on Automatic Control 67.4 (2021), pp. 2108–2115.
Karnik, N., Abdo, M. G., Estrada-Perez, C. E., Yoo, J. S., Cogliati, J. J., Skifton, R. S., ... & Manohar, K. (2024). “Constrained optimization of sensor placement for nuclear digital twins.” IEEE Sensors Journal. (published 02/28/2024)
Karnik, N., M. G. Abdo, and K. Manohar. “Optimal Sparse Sensor Placement with Adaptive Constraints for Nuclear Digital Twins." 75th Annual Meeting of the APS Division of Fluid Dynamics (APS DFD 2022) November 20-22, 2022, Indianapolis, IN.
DICE 2024: presentation about applications of sparse sensing in nuclear digital twins.
Karnik, N., Abdo, M. G., Manohar K. “Data-Driven Sensor Placement for Nuclear Reactor Transient Analyses in Digital Twins”. Bulletin of the American Physical Society
AI Institute in Dynamic Systems CTF workshop (Sponsored by NSF)
PHSOR 2024, Scintific ML workshop: “Sparse sensing and Sparse Learning for Nuclear Digital Twins.”
References