## Slide 1: Using Stochastic Collocation for Generalized Polynomial Chaos in RAVEN
RAVEN Training

## Slide 2: Nomenclature
is the response from a model (e.g., PCT)
Uncertain inputs to model:
  Material Properties
  Boundary Conditions
  Initial Conditions
Goal: What range of values can have as a result of uncertainties in ?

## Slide 3: Stochastic Polynomials
Expand model as combination of polynomials
Polynomial Representation
  Given a quantity of interest:
  Represent as combination of polynomials:
    Simpler to evaluate
    Easy to get statistical moments
    Less effort and more accurate than Monte Carlo
Notes: Important points:
- Polynomials are orthonormal
- Coefficients c_k are obtained by integration
- Polynomial set \Lambda is chosen by the user (or adaptively)

## Slide 4: Stochastic Collocation
Effectiveness depends on:
  Regularity of quantity of interest
  Polynomial expansion order
  Polynomial combination indices
  Sparse Grid quadrature types (Gauss, Clenshaw)
  Number of uncertain inputs
Tensor Product: Overkill
Total Degree: For Analytic Responses
Hyperbolic Cross: For Irregular Responses
Notes: This slide is an opportunity to talk about when SCgPC works well, and how we choose polynomials for expansion

## Slide 5: Model: Ballistic Motion
Quantity of Interest
  Range of Projectile
Variables
  Initial launch angle
    Low: 25 degrees
    High: 65 degrees
  Initial Velocity
    Low: 15 m/s
    High: 45 m/s

## Slide 6: Three Examples
Total Degree index set
First, Second, Third order polynomials
Sample points for ROMs
Train ROMs
Write ROMs to file
See “scgpc_trainer_1.xml” (and 2, and 3)

## Slide 7: Validate and Compare
Check validity of ROMs against original model
Sample original model (MC, Grid, LHS)
Load ROMs from file
Sample ROMs with same samplers
Plot results
See “mc.xml”, “grid.xml”, “lhs.xml”

## Slide 8: Results: Monte Carlo (200 samples)
Notes: Note that the first-order polynomials fail to capture any effect from the angle, and undershoot the maximum range quite a bit.

## Slide 9: Results: Monte Carlo (200 samples)
Notes: Basically identical to MC results

## Slide 10: Results: Monte Carlo (200 samples)
Notes: Basically identical to MC results

## Slide 11: Conclusions
Polynomial ROMs
  Cheap to create
  Fast to evaluate
  Accurate
Exceptions
  High dimension input space
  Irregular response