## Slide 1
Genetic Algorithms Optimizers

## Slide 2: Genetic Algorithms: Overview
Why Genetic Algorithms?
  Metaheuristic algorithms stem from biological evolution.
  Preferred for non-differentiable, expensive to differentiate, or objective functions with no intrusive access (black-box).
  Doesn’t get stuck in local minima, and hence works with non-convex problems.
  Can handle both constrained and unconstrained problems.
  Due to the encoding/decoding step it works with discrete, continuous, or mixed design spaces, with binary, integer, real, gray, or permutation encoding.
2

## Slide 3: Notation
 | G1 | G2 | G3 | G4 | G5
ch1 |  |  |  |  | 
ch2 | 2 | 5 | 1 | 8 | 4
ch3 |  |  |  |  | 
ch4 |  |  |  |  | 
ch5 |  |  |  |  | 
ch6 |  |  |  |  | 
ch7 |  |  |  |  | 
2 | 5 | 1 | 8 | 4
Population
2
Gene (variable)
2
Allele (value of variable)
Chromosome/individual (possible solution)
3

## Slide 4: Flowchart and Corresponding Input
4

## Slide 5: Overview of GAs
Encoding/decoding: Phenotype/Genotype variable representation (binary, integer, permutation, or real representation).
Steps
  Create initial population
  Fitness evaluation
  Parent selection
  Crossover: creation of offsprings
  Mutation: creation of mutated offsprings
  Replacement/repair
  Survivor selection
  If Termination condition(s) is met terminate, else repeat Steps 3 through 7 (each iteration is a generation).
Source: A Visual Guide to Evolutionary Strategies. https://blog.otoro.net/2017/10/29/visual-evolution-strategies.
5

## Slide 6: Evolutionary Operators of GAs
Parent selectors:
  Roulette Wheel
  Tournament Selection
  Rank Selection
Chart: 
| P1 | P2 | P3 | P4 | P5 | P6
Fitness | 5 | 8.2 | 1.4 | 0.98 | 2 | 2.3
Individual | Fitness
P1 | 5
P2 | 8.2
P3 | 1.4
P4 | 0.98
P5 | 2
P6 | 2.3
6

## Slide 7: Evolutionary Operators of GAs
Crossovers:
  One Point
  Two points
  Uniform
7

## Slide 8: Evolutionary Operators of GAs
Mutators:
  Swap Mutation
  Scramble Mutation
  Bit Flip Mutation
  Inversion Mutation
8

## Slide 9: Evolutionary Operators of GAs
  Survivor selection:
  Fitness Based
  Age Based
Generation/population i
Generation/population i+1
offsprings
Fitness
Chromosome
Fitness
Chromosome
Fitness
Chromosome
9

## Slide 10: Demonstration: Initial Loading Simplified Problem
Settings:
  1/4th of the core (PWR)
  56 variables (56 assembly locations to arrange)
  5 Materials (5 assembly types to “choose” from):
    Material - 1: Enrichment 2.2% in U235, No burnable poisons
    Material – 2: Enrichment 2.5% in U235, No burnable poisons
    Material – 3: Enrichment 2.5% in U235, burnable poisons (8.e-06 #/(cm*barn))
    Material – 4: Enrichment 3.5% in U235, No burnable poisons
    Material – 5: Enrichment 3.5% in U235, burnable poisons (8.e-06 #/(cm*barn))
  Objective:
    Maximization of cycle length
    The cycle length is determined based on a criticality search calculation (Soluble Boron Search): if SB <= 5 ppm, cycle ends
2D – Benchmark configuration
10

## Slide 11: Data Flow in Fuel Reload Optimization Platform
Risk-Informed Multi-Physics Uncertainty Analysis
[Constraints]
Design limits
Safety goals
[Objectives]
Max. energy production
Min. fuel cost
Core Design (e.g., PARCS and SIMULATE)
EFPD, Burnup, HCF
Boron concentration
Additional metadata
Core specification
Fuel inventory
Perturbed input files
System Analysis (RELAP5-3D)
Safety parameters
PCT, DNBR, HTC
Additional metadata
DBA scenarios
Core map and data
Perturbed input files
Fuel Performance (TRANSURANUS)
PCT, RIP, Oxidation
FFRD related data
Additional metadata
Fuel rod modeling
Core and TH data
Perturbed input files
Genetic Algorithm
EFPD: Effective full power day
HCF: Hot channel factor
DBA: Design basis accident
PCT: Peak cladding temperature
DNBR: Departure of nucleate boiling rate
HTC: Heat transfer coefficient
TH: Thermal-hydraulics
RIP: Rod internal pressure
FFRD: Fuel failure, relocation and dispersal

## Slide 12: Case Study: Single-objective Optimization for Core Design Introduction
Settings
  PWR core with 157 fuel assemblies (FA)
  Quarter-core symmetry
  6 FA designs → design space = 7.1⨉1032
  200 Population w/ 90 Iteration for GA
Constraints
  FQ (Heat flux hot channel factor) < 2.1
  FΔH (Nuclear enthalpy rise hot channel factor) < 1.48
  Peak critical boron concentration (CBC) <1300 pcm
Fuel type ID | 0 | 1 | 2 | 3 | 4 | 5
Enrichment (wt%) | 2 | 2.5 | 2.5 | 3.2 | 3.2 | Reflector
Burnable poison | None | None | 16 Gd rods | None | 16 Gd rods | -
Objectives
  Maximize cycle length (cycle energy production)
Exemplary 1/8 Core of a generic PWR
NOTE: FQ and FΔH are peaking factors used to characterize core power distribution in terms of ratios of local maximum power output to average core output.

## Slide 13: Case Study: Single-objective Optimization for Core Design Demonstration

## Slide 14: Case Study: Single-objective Optimization for Core Design Demonstration
Optimized Fuel Loading Pattern
Initial Fuel Loading Pattern

## Slide 15: User-defined objective function via external models
15
RAVEN XML Input
External Model

## Slide 16: User-defined Constraints in the external model/and Functions
16
RAVEN XML Input
In <optimizer>:

## Slide 17: User-defined Constraints in the external model/and Functions
17
Must be exactly named
Must be consistent with xml

## Slide 18: Hands-on Session
18

## Slide 19: Hands-on session
19
Unconstrained Discrete Optimization:
Mathematical formulation:
is the objective function.
represent boundary or box constraints.
G represents the functional constraints including explicit (i.e., involving inputs only), as well as implicit (i.e., involving both inputs and objective variable).

## Slide 20: Exercise1 (1_GA_MaxwRep.xml)
20
Maximize with replacement
Given:
where G=6 is the number of Genes (i.e., variables)
a discrete uniform distribution bounded by lb = 2, and ub = 7
y(x) = , is the objective function

## Slide 21: Exercise1 (1_GA_MaxwRep.xml)
21
Procedure: change directory (cd) to: ~/projects/raven/doc/workshop/optimizer/GeneticAlgorithms/exercises/ (For windows you might need to add double quotes)
Add a uniform discrete distribution that uses a “withReplacement” strategy.
Enable ‘onePointCrossover’ to occur 80% of the time and ‘swap mutation’ 90% of the time.
Build your objective function shown in the starter xml. (Hint use slide 13)
Add an objective function name in the xml that is consistent with your external model.
Run using the command: raven_framework 1_GA_MaxRep.xml
7 | 7 | 7 | 7 | 7 | 7
Analytic Solution:
Optimal value =

## Slide 22: Exercise2 (2_GA_MinRep.xml)
22
Minimization without replacement
Given:
where G=6 is the number of Genes (i.e., variables)
a discrete uniform distribution bounded by lb = 2, and ub = 7
y(x) = , is the objective function

## Slide 23: Exercise2 (2_GA_MinwoRep.xml)
23
Procedure:
Pick ‘rouletteWheel’ as the parent selector.
Set ‘survival selection’ criterion to ‘fitnessBased’
Set population size to 20 and max number of iterations (samplerInit limit to 15)
Run: raven_framework 2_GA_MinwoRep.xml
7 | 6 | 5 | 4 | 3 | 2
Analytic Solution:
Optimal value =

## Slide 24: Exercise3 (Maximization with explicit constraints) start from the starter exercise 2
24
Maximize without replacement
where G=6 is the number of Genes (i.e., variables)
a discrete uniform distribution bounded by lb = 2, and ub = 7
, is the objective function
Constraints:

## Slide 25: Exercise3
25
Procedure:
Go to Models/Constraints.py and name the first function ‘constrain’ this is a must since RAVEN searches for that exact word
Give the first explicit constraint function a name and make sure it is the same name you use in the XML. And implement the constraint x3 + x4 < 8.
Look at the second explicit constraint (Not used in the exercise).
In the XML starter input, Complete the functions block to define your constraint functions.
In the fitness block, change the penalty weighting of violation b to 20.
Fill the Constraint node at the end of the GA block to reflect the name of your constraint function.

## Slide 26: Exercise3 (Max w/o Rep with Constraints)
26
2 | 3 | 4 | 5 | 6 | 7
Analytic Solution:
Optimal value =
Unconstrained:
2 | 4 | 3 | 5 | 6 | 7
Constrained:
Raven’s Solution:

## Slide 27: Exercise4 (Continuous problem with implicit constraint)
27
Find v0, and the firing angle to Maximize the horizontal range of the projectile
where G=2 (v0, angle) is the number of Genes (i.e., variables)
a continuous uniform distribution bounded by lb = 10, and ub = 170
, is the objective function
Constraints: 250 (Is it explicit or implicit)?

## Slide 28: Exercise4 (Continuous problem with implicit constraint)
28
Procedure:
Add the missing variable to the <Models>and <Functions> blocks
Change the fitness to ‘feasibleFirst’ and the weight of the penalty (b) to 20
Fill the <ImplicitConstraint> to match the <Functions>
Add the missing variable to the <DataObjects>, and <OutStreams>

## Slide 29: Exercise4 (Continuous problem with implicit constraint)
29
170 | 24
Analytic Solution: =170,angle =
Optimal value = 2213.13
Raven’s Solution:

## Slide 30: Exercise4 (Continuous problem with implicit constraint)
30

## Slide 31: Non-Dominated Sorting Genetic Algorithm-II (NSGA-II)
A multi-objective optimization problem can be written as
  Minimize (or maximize)
  Subject to
  is m-th objective, where m = 1, 2, …, M.
  is j-th inequality constraint, where j = 1, 2, …, J
  is k-th equality constraint, where k = 1, 2, …, K
  x = is a n-dimensional vector
  and are the lower and upper bounds on i-th variable
Multiple optimal solutions
Multi-objective optimization problem subject to constraints
Multi-objective optimization technique
Higher-level information (or operator’s decision)
One optimal solution
NSGA-II is…
  Multi-objective, fast non-dominated sorting elite GA
Why NSGA-II?
  Lower computational complexity than NSGA-I
  Population diversity is guaranteed.
  One of the multi-objective evolutionary computation benchmark

## Slide 32: Non-Dominated Sorting Genetic Algorithm-II: Workflow
Initialize population (size N)
Start
Evaluate objectives & constraints
Rank population (based on rank and crowding Distance)
Parent selection
Crossover
Mutation
Evaluate objectives and constraints
Combine parents and offspring
Rank population
(based on rank and crowding Distance)
Select N individuals
Terminate?
offspring created
Elitism
Stop
Yes
No

## Slide 33: Non-Dominated Sorting Genetic Algorithm-II: Elitism
Minimize
Minimize
Parent
Offspring
Pareto front
Non-convex area
Feasible region
: first objective function
: second objective function
Keep the best chromosomes from parent and offspring population
Elitism does not allow an already found optimal solutions to be deleted.

## Slide 34: Non-Dominated Sorting Genetic Algorithm-II: Dominance Depth Method
Minimize
Minimize
Minimize
Minimize
Front-1
Front-2
Front-3
Front-4
Assign rank to each chromosome using the dominance depth
Non-dominated points belong to first rank.
The non-dominated solutions from remainder are in second rank, and so on.

## Slide 35: Non-Dominated Sorting Genetic Algorithm-II: Niching for the first rank
Niching gives preference to chromosomes that are not crowded.
Crowding distance measures crowdedness of a chromosome w.r.t. its neighbors lying on the same front.
  Crowding distance = a + b
  a and b are normalized distances.
Chromosomes from the first rank are selected based on niching.
Minimize
Minimize
a
b

## Slide 36: Case Study: Multi-objective Optimization for Core Design Introduction
Settings
  PWR core with 157 fuel assemblies (FA)
  Quarter-core symmetry
  6 FA designs → design space = 7.1⨉1032
  100 Population w/ 50 Iteration for GA
Constraints
  FQ (Heat flux hot channel factor) < 2.1
  FΔH (Nuclear enthalpy rise hot channel factor) < 1.48
  Peak critical boron concentration (CBC) <1300 pcm
Fuel type ID | 1 | 2 | 3 | 4 | 5 | 6
Enrichment (wt%) | Reflector | 2 | 2.5 | 2.5 | 3.2 | 3.2
Burnable poison | - | None | None | 16 Gd rods | None | 16 Gd rods
Objectives
  Maximize cycle length (cycle energy production)
  Minimize fuel cost
Exemplary PWR Core
NOTE: FQ and FΔH are peaking factors used to characterize core power distribution in terms of ratios of local maximum power output to average core output.

## Slide 37: Case Study: Multi-objective Optimization for Core Design Optimal Core Patterns
Cycle length (EFPD) | 364.10
Fuel cost (M$) | 499.45
FQ | 2.092
CBC (ppm) | 1295.6
FΔH | 1.479
Cycle length (EFPD) | 373.80
Fuel cost (M$) | 508.28
FQ | 2.090
CBC (ppm) | 1293.9
FΔH | 1.466
Cycle length (EFPD) | 383.50
Fuel cost (M$) | 520.92
FQ | 2.098
CBC (ppm) | 1296.8
FΔH | 1.476
Solution #3
Solution #1
Solution #2
Solution #1
Solution #2
Solution #3

## Slide 38: Case Study: Multi-objective Optimization for Core Design Common Features of Optimal Core Designs
All three core designs present the Low Leakage Loading pattern (L3P)
  Low/medium reactivity fuel at inner region to reduce the power peaking at core center
  High reactivity fuel at outer region to balance the power
  Use of burnable poison to suppress the excess reactivity
  Low reactivity fuel at core boundary to reduce the leakage / increase the neutron economy
Solution #3
Solution #1
Solution #2

## Slide 39: RESULTS

## Slide 40: Case Study: Multi-objective Optimization for Core Design Feasible Region and Pareto Frontier
NOTE: Feasible region: Search space region where all constraints are complied; Pareto frontier: Set of optimal solutions

## Slide 41: Conclusion & Future Works
Presented the PRLO platform, aimed at AI-driven reactor core design for addressing real-world challenges.
Demonstrated constrained multi-objective core design optimization problem for a 17 × 17 PWR core to minimize fuel cost and maximize fuel cycle length.
Future works include…
Conducting a full-scale demonstration of a PWR core design incorporating safety analysis.
Enhancing multi-objective optimization capabilities
Adaptive mutation/crossover
Active subspace exploration
More convergence criteria
Coupling with other metaheuristic optimizers (Any colony, Particle Swarm, Simulated Annealing)

## Slide 42
Sponsors, Partners, and Customers

## Slide 43
Completed Work (~FY24)
Demonstration of Genetic Algorithm-based optimization framework with single/multi-objective(s).
Design of optimized reactor core which considers system safety analysis and fuel performance, thus multi-physics methodology.
Reports are available at: https://www.osti.gov/
September FY21
August FY22
December FY22
March FY23
September FY23

## Slide 44
References
Nguyen, K., Hou, J., Abdo, M. G., Kim, J., Wang, C., & Choi, Y. J. (2023). Optimization of Light Water Reactor Core Design using a Genetic Algorithm in the RAVEN Framework. Transactions of the American Nuclear Society, 128, 664-667. https://doi.org/10.13182/T128-42064
Heo, Y., So, E., Abdo, M., Parisi, C., Choi, Y. J., Valeri, J., ... & Alfonsi, A. (2022). Demonstration of the Plant Fuel Reload Process Optimization for an Operating Pressurized Water Reactor (PWR). In 16th International Conference on Probabilistic Safety Assessment and Management, PSAM 2022.
So, E., Heo, Y., Abdo, M. G., Alfonsi, A., & Choi, Y. J. (2022). Development of Genetic Algorithms for Plant Reload Optimization for an Operating Pressurized Water Reactor. In 16th International Conference on Probabilistic Safety Assessment and Management, PSAM 2022.

## Slide 45
Thanks for attention!
Questions?

## Slide 46: Backup Slides
46

## Slide 47
47
Analytic Solutions

## Slide 48: Enhancements and Acceleration
    Exploring the active subspace hosting the search directions that increase the fitness then constrain the mutation to these directions.
    Accelerate GA with Markov Chains.
    Recast the problem as a reinforcement learning problem:
      Objective: Maximize Cycle length or minimize # feeds.
      Constraints: enrichment, number of GAD/burnable poison, Kinf, PPF, FDH, …
      Action Space: Discrete fuel inventory
      State Space: Fuel enrichment in each location.
      Game Rules:
        Do not violate constraints.
        Do not place specific fuels next to each other (e.g., no GAD fuels horizontally or vertically adjacent).
    Hybridizing and/or benchmarking with other metaheuristic methods: Particle Swarm, Ant colony, Bee algorithms, etc.
48

## Slide 49: NSGA-II: Survivor Selection
P(t)
Q(t)
Non-dominated sorting
Size = 2N
Crowding distance sorting
Rejected
Size = N
Combine parent and offspring populations and choose the best N solutions for next generation
Notes: This slide shows how survivors from merged population are selected. We have N size of parent population and N size of offspring population, and the task is we have to select the N best solutions for t+1 generation.
What we do here is we combine them and perform non-dominated sorting. Graphically you can see that some solutions will lying in front 1, front 2, and front 3 and so on. Thereafter, we will select the solutions one by one. Since size of front 1, front 2 and front 3 are small so it can be accommodated within N. Now since there is a space available to make the size N, we are going to include the part of solutions in front 4. The solutions in front 4 will be sorted in a descending order. So the solutions which are coming on the top of front 4 box, they will be selected so that all these solutions will constitute N number of population.
So, solutions below the dotted line will be rejected.

## Slide 50: NSGA-II: Pseudo Code
Algorithm 1: NSGA-II |  | 
1: | Solution representation, t :=0 (generation counter), maximum allowed generation = T; | 
2: | Initialize random population (P(t)); | 
3: | Evaluate (P(t)) and assign rank using dominance depth method and diversity using crowding distance operator to P(t); | 
4: | While t < T do | 
5: |  | M(t) := ParentSelection(P(t)) (Crowded Binary Tournament Selection);
6: |  | Q(t) := Variation(M(t)); (Crossover and Mutation)
7: |  | Evaluate Q(t);
8: |  | Merge population: = P(t) Q(t);
9: |  | Assign rank using dominance depth method and diversity using crowding distance operator to ;
10: |  | P(t+1) = Survivor();
11: |  | t := t+1
12: | End while | 
Algorithm 1: NSGA-II |  | 
1: | Solution representation, t :=0 (generation counter), maximum allowed generation = T; | 
2: | Initialize random population (P(t)); | 
3: | Evaluate (P(t)) and assign rank using dominance depth method and diversity using crowding distance operator to P(t); | 
4: | While t < T do | 
5: |  | M(t) := ParentSelection(P(t)) (Crowded Binary Tournament Selection);
6: |  | Q(t) := Variation(M(t)); (Crossover and Mutation)
7: |  | Evaluate Q(t);
8: |  | 
9: |  | 
10: |  | 
11: |  | t := t+1
12: | End while | 

## Slide 51: NSGA-II: Pseudo Code
Algorithm 2: Crowding distance (F)
1: r = ¦F¦
2: set for each i F
3: for each objective m do
4: F = sort(F, m)
5:
6: for i=2 to (r-1) do
7:
8: end for
9: end for
Algorithm 2: Crowding distance (F)
1: r = ¦F¦
3: for each objective m do
4: F = sort(F, m)
6: for i=2 to (r-1) do
8: end for
9: end for
Minimize
Minimize
1
i-1
i
i+1
r
Front-F solutions

## Slide 53: Thank you for your attention