## Slide 1
Bayesian Model Calibration
July 18, 2024

## Slide 2: Forward UQ vs. Inverse UQ
* X. Wu, Inverse uncertainty quantification, 2020

## Slide 3: Model Calibration (Inverse UQ)
Motivation
  To address the “missing input uncertainty information” issue
  To develop a rigorous method to infer the uncertainties in input parameters
  The process to inversely quantify input uncertainties based on simulation and experimental data
Objective
  Capture the input uncertainties, rather than the best-fit point estimates
  Avoid over-fitting via explicitly considers model uncertainty
  Reduce computational cost through machine learning techniques

## Slide 4: Problem Definition: Role of Model Calibration
A general simulation model with:
  : design/controllable/observable variables (i.e., initial/boundary conditions)
  : calibration parameters (i.e., physical constants and tuning parameters), usually subjected to unknown uncertainties (aleatory, epistemic or mixed).
Given experimental data , inversely quantify the parameter uncertainties in such that is consistent with
  Model updating equation:
  : model uncertainty/discrepancy
  : measurement noise, usually assumed to be i.i.d. zeo-mean Gaussian
Goal: estimate the calibration parameters, , using field observations and computational model

## Slide 5: Bayesian Inference: Bayes’ Rule, Prior, Likelihood, Posterior
Prior: Knowledge about before observing the data
Likelihood: probability to observe given certain values of
Posterior: updated knowledge about after observing the data
Posterior
Likelihood
Prior

## Slide 6: General Look at Bayes Rules
Posterior PDF describes uncertainty in given data
Prior PDF for is required
Inference proceeds through the samples from posterior distribution

## Slide 7: Metropolis-Hastings Recipe for MCMC
Initialize chain at
Given current realization of , generate from a symmetric distribution
Compute the acceptance probability
Set with probability , otherwise
Iterate previous three steps

## Slide 8: The Process of Model Calibration

## Slide 10: Model Calibration Challenges
Challenge 1
  Model calibration under uncertainty
Challenge 2
  Holistic tool to perform sensitivity analysis, uncertainty quantification and model calibrations
Challenge 3
  Computational expensive: requires thousands of simulations
Challenge 4
  Slow convergence with high-dimensional input space and output space

## Slide 11: RAVEN Likelihood Model
https://github.com/idaholab/BayCal
https://baycal.readthedocs.io/en/latest/index.html#

## Slide 12: Fission Gas Release (FGR) and Problem Definition
Swelling, gap pressure build-up, thermal conductivity degradation
Significant inherent uncertainties in FGR modeling
The FGR model in BISON has 5 input parameters whose uncertainties are only known by “expert opinion”.

## Slide 13: RAVEN Model Calibration
Markov Chain Monte Carlo
  Metropolis-Hastings algorithm with dimensionality reduction
  Adaptive Metropolis algorithm with dimensionality reduction
Riso AN3 Benchmark: https://mooseframework.inl.gov/bison/LWR/validation/Riso_AN3/doc/Riso_AN3.html

## Slide 14: Application 2
Data analytics methods to integrate measured data and simulation models to reconstruct core power profile (i.e., solve the inverse problem)