## Slide 1: Advanced Reliability and Safety Analysis
RAVEN Workshop

## Slide 2: Outline
Dynamic Probabilistic Risk/Safety Analysis
  Classic vs. Dynamic PRA
Adaptive Sampling
  Limit Surface

## Slide 3: Reliability and Safety Analysis
Safety Analysis: determine the likelihood a system will not perform its functions in a specified time period
Reliability Analysis: determine the ability of a system to perform its functions in a specified time period

## Slide 4: Dynamic Probabilistic Risk/Safety Analysis
Classic Probabilistic Risk/Safety Analysis
  Static boolean logic structures
    Event-Trees / Fault-Trees
  Accident sequence set by the analyst
  Timing of events partially considered
Dynamic Probabilistic Risk/Safety Analysis
  Direct use of system simulation codes
  Coupled with stochastic analysis tools (e.g., RAVEN)
  Accident sequence set by the system control logic
  Timing of events fully considered

## Slide 5: Dynamic Probabilistic Risk/Safety Analysis
Stochastic analysis
Sample the pdfs
Run N times system simulation code(s)
Evaluate desired FOMs
Deterministic modeling
Plant modeling
External event modeling
Stochastic modeling
Identify uncertain parameters and associate a pdf

## Slide 6: ROMs: Classifiers
ROMs as mathematical models designed approximate an input-output relationship
Classifiers: output variable is boolean
  i.e., 0 or 1
  e.g., OK or Failure

## Slide 7: Exercise 1: Dynamic PRA Analysis

## Slide 8: Excercise1: Model Sampling
Model
  Simplified PWR model
Scenario
  Station Blackout Analysis
Steps
  Sample the model response N times
  Determine failure probability

## Slide 9: Excercise1: Model Sampling
Initial cooling
Cooling failure
Cooling recovered
t_SBO
t_REC

## Slide 10: Excercise1: Model Sampling
Input file name: dynamicPRA.xml
Distributions
<Steps>
<MultiRun name="MCRun">
<Input class="DataObjects" type="PointSet" >inputPlaceHolder</Input>
<Model class="Models" type="ExternalModel" >PythonModule</Model>
<Sampler class="Samplers" type="MonteCarlo" >MC</Sampler>
<Output class="DataObjects" type="PointSet" >outPS</Output>
<Output class="DataObjects" type="HistorySet" >outHS</Output>
</MultiRun>
...
<PostProcess name="PP">
<Input class="DataObjects" type="PointSet" >outPS</Input>
<Model class="Models" type="PostProcessor" >integral</Model>
<Output class="Files" type="" >integral.xml</Output>
</PostProcess>
</Steps>
Steps
Samplers
Models
Databases
DataObjects

## Slide 11: Exercise 2: Limit Surface Analysis

## Slide 12: Adaptive Sampling
Computational costs might be impractical
  Computationally expensive codes
  Many simulation runs are often required
Reduced Order Modeling can be a solution
  Objective: reduce the complexity of the problem
Search of the limit surface: boundaries in the input space between failure and success
Ω

## Slide 13
Reliability Analysis: Limit Surface Search
Train a surrogate model
Use the surrogate model to determine an approximation of the limit surface
Choose a set of samples on the approximated limit surface
Run the “real” model to verify the approximation
Generate a set of training simulations to sample the plant response
Reach convergence
No
Yes
Stop

## Slide 14
Define the distributions:
  Weigh the error estimation
  Generate a probability-weighted metric for grid construction
  Determine the probability of being inside one of the regions identified by the limit surface
  Define the surrogate model (acceleration ROM) to be used as the adaptive sampler
Define the adaptive sampler:
  Convergence control and grid
  Import the acceleration ROM
  Associate the distribution with the variables
Define the adaptive sampling step
Reliability Analysis: Limit Surface Workflow

## Slide 15: Exercise 2: Limit Surface Analysis
Input file name: runLS.xml
Distributions
<Models>
...
<ROM name="ROM" subType="SciKitLearn">
<Features>tREC,tSBO</Features>
<Target>goalFunction</Target>
<SKLtype>svm|SVC</SKLtype>
<kernel>rbf</kernel>
<gamma>0.25</gamma>
<C>25</C>
</ROM>
</Models>
Steps
Samplers
Models
Functions
DataObjects

## Slide 16: Exercise 2: Limit Surface Analysis
Input file name: runLS.xml
Distributions
<Functions>
<External name="goalFunction" file="goalFunction">
<variable>outcome</variable>
</External>
</Functions>
Steps
Samplers
Models
Functions
DataObjects
def __residuumSign(self):
if self.outcome == 0:
return -1
else: return 1
File: goalFunction.py

## Slide 17: Exercise 2: Limit Surface Analysis
Input file name: runLS.xml
Distributions
<Samplers>
...
<LimitSurfaceSearch name="Adaptive">
<ROM class="Models" type="ROM" >ROM</ROM>
<Function class="Functions" type="External" >goalFunction</Function>
<TargetEvaluation class="DataObjects" type="PointSet" >outPS
</TargetEvaluation>
<Convergence limit="250" forceIteration="False" weight=”CDF"
persistence="10">1.0e-5</Convergence>
<variable name="tREC">
<distribution>tREC_dist</distribution>
</variable>
<variable name="tSBO">
<distribution>tSBO_dist</distribution>
</variable>
</LimitSurfaceSearch>
</Samplers>
Steps
Samplers
Models
Functions
DataObjects

## Slide 18: Exercise 2: Limit Surface Analysis
Input file name: runLS.xml
Distributions
<Steps>
<MultiRun name="MCRun" pauseAtEnd="True">
<Input class="DataObjects" type="PointSet" >inputPlaceHolder</Input>
<Model class="Models" type="ExternalModel" >PythonModule</Model>
<Sampler class="Samplers" type="MonteCarlo" >MC</Sampler>
<Output class="DataObjects" type="PointSet" >outPS</Output>
</MultiRun>
<MultiRun name="adaptive" pauseAtEnd="True">
<Input class="DataObjects" type="PointSet" >inputPlaceHolder</Input>
<Model class="Models" type="ExternalModel" >PythonModule</Model>
<Sampler class="Samplers" type="LimitSurfaceSearch">Adaptive</Sampler>
<SolutionExport class="DataObjects" type="PointSet" >limitSurface
</SolutionExport>
<Output class="DataObjects" type="PointSet" >outPS</Output>
</MultiRun>
</Steps>
Steps
Samplers
Models
Functions
DataObjects

## Slide 19: Exercise 3: Failure Probability Calculation from LS

## Slide 20: Exercise 3: Failure Probability Calculation From LS
Limit surface has a pure deterministic information
Probabilistic information is contained in the integral within the limit surface weighted by the set of distributions
For a new set of distributions the integral needs to be recalculated but the limit surface is unchanged
Ω

## Slide 21: Exercise 3: Failure Probability Calculation From LS
Input file name: pbFromLS.xml
Distributions
<Models>
<PostProcessor name="LS_Integral" subType="LimitSurfaceIntegral">
<tolerance>0.001</tolerance>
<integralType>MonteCarlo</integralType>
<target>goalFunction</target>
<variable name="tREC">
<distribution>tREC_dist</distribution>
</variable>
<variable name="tSBO">
<distribution>tSBO_dist</distribution>
</variable>
</PostProcessor>
</Models>
Steps
Samplers
Models
Databases
DataObjects

## Slide 22: Exercise 3: Failure Probability Calculation From LS
Input file name: pbFromLS.xml
Distributions
<Steps>
<IOStep name="extract_data_adapt">
<Input class="Databases" type="HDF5" >out_db_adaptive</Input>
<Output class="DataObjects” type="PointSet" >outAdapt_failure</Output>
</IOStep>
<PostProcess name="integral">
<Input class="DataObjects” type="PointSet" >outAdapt_failure</Input>
<Model class="Models" type="PostProcessor" >LS_Integral</Model>
<Output class="DataObjects” type="PointSet" >LSintegral_PS</Output>
<Output class="Files" type="" >integral.csv</Output>
</PostProcess>
</Steps>
Steps
Samplers
Models
Databases
DataObjects