## Slide 1: Ensemble Modeling
RAVEN Workshop

## Slide 2: Outline
RAVEN models: brief overview
Ensemble Modeling
  Overview
  Characteristics and limitations
Application examples of Ensemble Modeling
Hands-on:
  Example using 2 external models
  Example using the Code Interface we previously created

## Slide 3: RAVEN models: overview

## Slide 4: RAVEN models: a quick introduction
RAVEN categorizes in its Models entity the following sub-entities:
  Codes:
    Aimed to interface with physical codes (e.g. RELAP5-3D, etc.)
  ROMs:
    Aimed to emulate the response of a system based on a simplified mathematical representation
  External Models:
    Aimed to provide to the user an easy way to implement sets of equations directly in RAVEN
  Post-Processors:
    Aimed to analyze the generated datasets (e.g. Statistical moments, Data Mining, etc.)
  Ensemble Models:
    Aimed to assemble multiple models

## Slide 5: RAVEN ensemble modeling

## Slide 6: Ensemble Modeling Motivations
In several cases multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others
In order to face this “problem” in the RAVEN framework, a new model category (e.g. class), named EnsambleModel, has been designed
This class is able to assemble multiple models of other categories (i.e. Code, External Model, ROM), identifying:
  the input/output connections
  the order of execution
  the parallel execution strategy for each sub-model
EnsembleModel
Physics 1
Physics 2

## Slide 7: Ensemble Model
A new model entity (e.g., class), named EnsembleModel, has been developed:
  Assemble multiple models of other categories, identifying the input/output connections and the order of execution
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 8: Ensemble Model: Main Characteristics
The EnsembleModel entity has the following main characteristics:
  Ability to link all the RAVEN Models:
    Codes, ROMs, ExternalModels
  Practical no limit on the number of Models in the Ensemble configuration
  Capability to link the different Models through both scalar and vector variables (e.g. Max Cladding Temperature (scalar) or Power history (vector))
  Capability to transfer meta-data from the different models (e.g. restart files, etc.)
The current EnsembleModel entity is not indicated to handle high-density field data

## Slide 9
Model 1
Model N-1
Model N
Model 1
Model 2
Model 3
  Ensemble Model: Chain of Models
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 10
  Ensemble Model: Non Linear
Notes: Sometimes, multiple models need to interface with each other since the initial conditions of some are dependent on the outcomes of others

## Slide 11: Employing Ensemble Modeling in real applications

## Slide 12: Ensemble model for Multi-Unit Power Plant: 1st Configuration
Plant Logic Model
Unit 1
Unit 2
Unit 3
PWR1
SFP1
PWR2
SFP2
PWR3
SFP3
RAVEN ensemble model
Dynamic PRA for a Station Black Out Multi-Unit scenario

## Slide 13: Ensemble model for Multi-Unit Power Plant: 2nd Configuration
Plant Logic Model
Unit 1
Unit 2
Unit 3
PWR1
SFP1
PWR2
SFP2
PWR3
SFP3
RAVEN ensemble model
Exploiting the restart capability of the driven code, the EnsembleModel can be constructed through a chain of basic units that can be repeated, for example, over time
Human Actions
Plant Logic Model
Unit 1
Unit 2
Unit 3
PWR1
SFP1
PWR2
SFP2
PWR3
SFP3
RAVEN ensemble model
over time
10 minutes

## Slide 14: Ensemble model for Multi-Unit Power Plant: Preliminary results
4 Spent Fuel Pools
Transferring Restarts

## Slide 15: Employing Ensemble modeling in RAVEN: 2 Examples

## Slide 16
1-Dimensional heat conduction transient (in a slab of thickness L=1 m):
  EM1, heat conduction partial differential equation:
  EM2, thermal conductivity (input of EM1) as function of the average temperature in the slab boundary conditions:
EM1
EM2
  Ensemble Model: Example 1 specifications

## Slide 17: Workflow
Create EnsembleModel
Input File name: ensemble_model_ext_models.xml
Sample the model
Plot results

## Slide 18: Create an Ensemble model of a code and an ExternalModel
Samplers
Models
Distributions
Steps
Databases
DataObjects
<Distributions>
<Uniform name=’leftTemperatureDist'>
<upperBound>500</upperBound>
<lowerBound>1700</lowerBound>
</Uniform>
<Uniform name=’rightTemperatureDist'>
<upperBound>500</upperBound>
<lowerBound>1700</lowerBound>
</Uniform>
</Distributions>
Distribution specifications
OutStreams

## Slide 19: Create an Ensemble model of a code and an ExternalModel
Models
Distributions
<Models>
...
<ExternalModel name=’heatTransfer' subType=’’ ModuleToLoad=’EM1linear’>
<variables>leftTemperature,rightTemperature,k,solution</variables>
</ExternalModel>
<ExternalModel name=’thermalConductivityCompuation’ subType=’’ ModuleToLoad=’EM2linear’>
<variables>leftTemperature,rightTemperature,k,averageTemperature</variables>
</ExternalModel>
...
</Models>
Samplers
Steps
Databases
DataObjects
OutStreams
List of Models we are going to use

## Slide 20: Create an Ensemble model of a code and an ExternalModel
Models
Distributions
<Models>
...
<EnsembleModel name=’codeAndExtModel' subType=’’>
<Model class=’Models' type=’ExternalModel’>
thermalConductivityComputation
<Input class=“Files” type=“”>inputHolder</Input >
<TargetEvaluation class=’DataObjects’
type=’PointSet’>thermalConductivityComputationContainer
</TargetEvaluation>
</Model>
<Model class=’Models' type=’Code’>
heatTransfer
<Input class=“Files” type=“”>inputHolder</Input >
<TargetEvaluation class=’DataObjects’ type=’PointSet’>
heatTransferContainer</TargetEvaluation>
</Model>
</EnsembleModel>
...
</Models>
Samplers
Steps
Databases
DataObjects
OutStreams
Inputs of this model
Exclusive output

## Slide 21: Create an Ensemble model of a code and an ExternalModel
DataObjects
Distributions
Samplers
Steps
Databases
Models
OutStreams
<DataObjects>
<PointSet name=’heatTransferContainer'>
<Input>leftTemperature,rightTemperature,k</Input>
<Output>solution</Output>
</PointSet>
<PointSet
name=’thermalConductivityComputationContainer'>
<Input>leftTemperature,rightTemperature</Input>
<Output>k</Output>
</PointSet>
<PointSet name=’metaModelOutputTest'>
<Input>leftTemperature,rightTemperature</Input>
<Output>k,solution</Output>
</PointSet>
</DataObjects>
Link

## Slide 22: Create an Ensemble model of two model
Let’s run the code…

## Slide 23: Exercise 2: Create an EnsembleModel of a Code and an ExternalModel

## Slide 24
Also codes can be used in the Ensemble modeling.
  EM1: Code, Analytical Bateman
    Transmutation
  EM2: External Model, convert final outcomes of EM1 into atom densities
EM1
EM2
  Ensemble Model: Example 2 specifications

## Slide 25: Workflow
Create EnsembleModel
Input File name: ensamble_model_example.xml
Sample the model
Plot results

## Slide 26: Create an Ensemble model of a code and an ExternalModel
Samplers
Models
Distributions
Steps
Databases
DataObjects
<Distributions>
<Uniform name=’sigma'>
<upperBound>1000</upperBound>
<lowerBound>0.0</lowerBound>
</Uniform>
<Uniform name=’decayConstant'>
<upperBound>1.e-7</upperBound>
<lowerBound>1.e-8</lowerBound>
</Uniform>
</Distributions>
Distribution specifications
OutStreams

## Slide 27: Create an Ensemble model of a code and an ExternalModel
Models
Distributions
<Models>
...
<ExternalModel name=’convertToAtomDensity' subType=’’ ModuleToLoad=’toAtomDens’>
<variables>A,B,C,D,densA,densB,densC,densD</variables>
</ExternalModel>
<Code name=’testModel' subType=’GenericCode’>
<executables>ensembleModelWithCode/AnalyticalDplMain.py</executables>
<clargs arg=”” extension=’.xml’ type=’input’ />
<clargs arg=”” extension=’.csv’ type=’output’ />
<prepend>python</prepend>
</Code>
...
</Models>
Samplers
Steps
Databases
DataObjects
OutStreams
List of Models we are going to use

## Slide 28: Create an Ensemble model of a code and an ExternalModel
Models
Distributions
<Models>
...
<EnsembleModel name=’codeAndExtModel' subType=’’>
<Model class=’Models' type=’ExternalModel’ inputNames=’inPlaceHolder’>
convertToAtomDensity
<Input class=“Files” type=“”>referenceInput.xml</Input >
<TargetEvaluation class=’DataObjects’ type=’PointSet’>convertedData
</TargetEvaluation>
</Model>
<Model class=’Models' type=’Code’>
testModel
<Input class=“Files” type=“”>inputHolder</Input >
<TargetEvaluation class=’DataObjects’ type=’PointSet’>sampleMC</TargetEvaluation>
</Model>
</EnsembleModel>
...
</Models>
Samplers
Steps
Databases
DataObjects
OutStreams
Inputs of this model
Exclusive output

## Slide 29: Create an Ensemble model of a code and an ExternalModel
DataObjects
Distributions
Samplers
Steps
Databases
Models
OutStreams
<DataObjects>
<PointSet name=’convertData'>
<Input>A,B,C,D</Input>
<Output>densA,densB,densC,densD</Output>
</PointSet>
<PointSet name=’sampleMC'>
<Input>sigma-A,sigma-B,decay-A,decay-B</Input>
<Output>A,B,C,D</Output>
</PointSet>
<PointSet name=’finalResponses'>
<Input>sigma-A,sigma-B,decay-A,decay-B</Input>
<Output>A,B,C,D,densA,densB,densC,densD</Output>
</PointSet>
</DataObjects>
Link

## Slide 30: Create an Ensemble model of two model
Let’s run the code…

## Slide 31: Thank you Questions?